## Slide 1: Alaska Supplement
For use with Boat America and Boating Skills & Seamanship

## Slide 2: Boater Education
The Boat America course is a national course providing the Federal regulations and safety practices to ensure a safe boating experience for you and your families. The state of Alaska has some state-specific rules that are different. This presentation will review many of these Alaska state variances.

## Slide 3: Boater Education
No mandatory boater education required in Alaska.
For information on boating education:
Alaska Boating Safety Program (907) 269-8706 www.alaskaboatingsafety.org
Alaska Water Wise Courses (907) 269-8704 www.alaskaboatingsafety.org
Alaska Marine Safety Education Association (907) 747-3287 www.amsea.org
D 17 Coast Guard Auxiliary
wow.uscg.info/content.php?unit=170

## Slide 4: PWC Operation
Take both basic boating safety and PWC-specific courses and develop skills under the instruction of an experienced operator.
Operators must have the skill and ability to re-board the boat in deep water. When righting an overturned PWC, rotate it according to the decal on the transom.
Wear the right gear. Synthetic long underwear, a dry suit or a two-to-three-millimeter wet suit, neoprene boots, neoprene or water-ski gloves, safety helmet and goggles. In addition to these, a snug-fitting USCG-approved PFD is highly recommended and advised.
Notes: Operating a PWC in Alaska
Take both basic boating safety and PWC-specific courses and develop skills under the instruction of an experienced operator.
Operators must have the skill and ability to re-board the boat in deep water. When righting an overturned PWC, rotate it according to the decal on the transom.
Wear the right gear. Synthetic long underwear, a dry suit or a two-to-three-millimeter wet suit, neoprene boots, neoprene or water-ski gloves, safety helmet and goggles.
In addition to these, a snug-fitting USCG-approved PFD is highly recommended and advised.

## Slide 5: Boat Registration
All boats not specifically exempted, including documented boats, barges, sport fishing guide boats, and tenders are to be registered with the State of Alaska.
Online at: www.alaskaboatingsafety.org
Register at any Dept. of Motor Vehicles office or online: www.state.ak.us/dmv/reg/boat.htm
Registration is valid for three years.
8 digit number with validation decal
AK 2345 AB (decal)
AK-2345-AB (decal)
Notes: Registration Requirements.
For registration fees, contact the Alaska Office of Boating Safety
SECTION VIII. VESSEL REGISTRATION NUMBER
A. The number issued pursuant to these regulations shall be in accordance with the pattern described in this subsection.
1. The vessel registration number shall be divided into three parts, for the purpose of providing a combination of numerals and letters which furnish individual vessel registration numbers.
2. The first part of the number shall be an abbreviation in capital letters of the State of Alaska – AK –and shall be followed by an equivalent space.
3. The second part of the number shall be a group of digits consisting of four Arabic numerals appearing after the letters AK, and shall be followed by an equivalent space or hyphen.
4. The remainder of the number shall consist of no more than two capital letters, in sequence, in accordance with the serials numerically and alphabetically. As example:
5. Since the letters “I”, “O”, and “Q” may be mistaken for Arabic Numerals, all letters sequences using “I”, “O”, and “Q” shall be omitted. Objectionable words formed by the use of letters will not be used.

## Slide 6
Correct Display of Numbers
3’’ High
Contrasting colors
Sticker within 6 inches of AK Number
AK 2345 AB
AK 2345 AB
Port Side
Starboard Side
Notes: Display of numerals and decals on vessel.
1. The number awarded, exactly as shown on the certificate of numerals shall be painted on, or attached to, each side of the bow of the vessel for which it was issued.
2. The numerals shall be placed on each side of the forward half of the vessel in such position as to provide clear legibility for identification. The numerals shall read from left to right and shall be in block characters of good proportion not less than three inches in height. The numerals shall be of a color which will contrast with the background, and so maintained as to be clearly visible and legible; i.e., dark numerals on a light background or light numerals on a dark
background.
3. The commissioner will furnish to all applicants two (2) decals bearing the numbers of the year of expiration, which will establish valid registration. The decals are to be displayed on each side of the boat (within 6 inches) immediately following the assigned Alaska number.
AK 0234 AB (decal) or AK-0234-AB (decal)

## Slide 7: Boat Titling
All motorized boats over 24 ft. must be titled whether documented or undocumented.
When selling a boat, transfer the title to the new owner in order to be free of liability in the event of emergency, desertion, or other misuse of the vessel.
Notes: Registration Requirements.
For registration fees, contact the Alaska Office of Boating Safety
SECTION VIII. VESSEL REGISTRATION NUMBER
A. The number issued pursuant to these regulations shall be in accordance with the pattern described in this subsection.
1. The vessel registration number shall be divided into three parts, for the purpose of providing a combination of numerals and letters which furnish individual vessel registration numbers.
2. The first part of the number shall be an abbreviation in capital letters of the State of Alaska – AK –and shall be followed by an equivalent space.
3. The second part of the number shall be a group of digits consisting of four Arabic numerals appearing after the letters AK, and shall be followed by an equivalent space or hyphen.
4. The remainder of the number shall consist of no more than two capital letters, in sequence, in accordance with the serials numerically and alphabetically. As example:
5. Since the letters “I”, “O”, and “Q” may be mistaken for Arabic Numerals, all letters sequences using “I”, “O”, and “Q” shall be omitted. Objectionable words formed by the use of letters will not be used.

## Slide 8: Maximum Capacities
8
Capacity label by Manufacturer
Number of persons
Weight for persons, motor and gear
Maximum engine horsepower
Notes: Overloading and Overpowering.
No vessel may be loaded with passengers or cargo beyond its safe cargo carrying capacity.
The maximum persons capacity marked on a vessel's maximum capacities plate must not be exceeded.
The maximum weight capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe loading requirements.
Overpowering
No vessel may be operated beyond its safe powering capacity.
The maximum horsepower capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe powering requirements.

## Slide 9: Life Jackets
A USCG approved wearable personal flotation device (PFD) correctly sized and in serviceable condition is required to be on board for every person regardless of vessel type.
Boats 16 feet and longer must additionally carry a USCG approved throwable device (except canoe or kayak in Alaska).
PFDs with water impact ratings are suggested for high-speed watersports such as operating PWC and being towed.
Persons under 13 must wear a life jacket when in an open boat, on the deck of a boat, or when being towed (i.e., tubing, waterskiing)
Notes: AK Personal Flotation Devices (PFD)
All vessels, except sailboards, must carry one wearable U.S. Coast Guard-approved Type I, II, III, or V PFD for each person on board.
Ion addition, vessels 16 feet in length or longer must have one U.S. Coast Guard-approved Type IV PFD on board and readily accessible.
Children under 13 years of age must wear a U.S. Coast Guard-approved. Type I, II, III, PFD at all times while underway on the open deck of any vessel.
Anyone under 13 years of age being towed behind a vessel must wear a U.S. Coast Guard-approved. Type I, II, III, PFD.

## Slide 10: Water Skis
It is highly advisable and safer that persons wear a PFD while being towed.
Waterskiing at night is prohibited
The towing boat must have 12 year or older observer or a rear-view mirror.
Notes: AK Water Skis and Surfboards
Water Skiing
To make water skiing safer and more enjoyable, boat operators and skiers should observe the following:
Operate only between sunrise and sunset.
Boat operators must either have another person (12 years of age or older) onboard as a lookout or have a rear-view mirror installed on the boat.
The boat operator should keep a minimum of a 200-foot wide “ski corridor” (100 feet on either side) to protect the skier from other boats and/or obstacles.
A boat operator may not tow a person on water skis, a surfboard, or a similar device, in a reckless or negligent manner so as to endanger the life or property of another person (AS 05.25.060 (1)).
In order to be safe, it is advisable that skiers should wear a PFD that is approved by the U.S. Coast Guard for the activity. Inflatable PFDs are not appropriate for water skiing.

## Slide 11: Boating While Intoxicated
Alaska law defines Boating Under the Influence (BUI) as having a Blood Alcohol Count (BAC) level of 0.08 or higher
Law enforcement may also consider certain specific behaviors as a cause for conducting a BUI investigation.

## Slide 12: Water Skis & Towing
Within Alaska state waters it is permissible to tow at night with great care.
Illegal to operate a vessel towing while intoxicated as defined in previous slide.
Although not illegal, it is highly inadvisable to ski or be towed while intoxicated.
Stay clear of no ski zones –
  No towing within 200 feet of commercial boat dock, moorage harbor, swim area

## Slide 13: Cold Water Survival
ALWAYS wear a life jacket when in and on an open boat.
Carry a communication device or signaling device, VHF, EPIRB, whistle, cell phone, etc.
Equip the boat with a re-boarding ladder or other device.
Carry readily accessible Type IV and other throwable devices.
Cold water immersion events happen quickly. To aid in your survival:
Notes: Cold Water Survival
Prepare for Cold Water Immersion
Most immersion events happen quickly and unexpectedly. So, while prevention is best, it is also important to be prepared. Taking these simple steps will help ensure the best possible outcome:
Always wear a life jacket when in an open boat or on an open boat deck. Trying to put your PFD on in cold water is extremely difficult (if not impossible) and costs precious time and energy.
Carry some communication and signaling devices ON YOUR PERSON. A personal locator beacon, a small hand held VHF radio, EPIRB, a cell phone in a waterproof bag, a whistle, and some visual distress signals may save the day. Today’s devices are smaller, lighter and easy to carry.
Unless the boat is designed so that a person in the water can easily get back into the boat unassisted, equip the boat with a re-boarding ladder, rope ladder, foot sling or a swim platform.
Carry immersion (survival) suits. Make sure they are well maintained and readily accessible.
Practice re-boarding your boat, donning survival suits, signaling, transmitting MAYDAYs, recovering a person overboard, and other cold-water survival techniques described in this section. Drills are fun and build skill and confidence.

## Slide 14: Cold Water Survival
Cold Water Immersion:
  According to Fatality Statistics cold water immersion is the #1 threat to Alaska boaters
  1-10-1 Principle works only if you are wearing a lifejacket!
    1 minute to get your breathing settled (Survive the initial immersion)
    10 minutes of meaningful activity (Self rescue possible during this time)
    1 hour of consciousness
Notes: Cold Water Survival
Hypothermia
Hypothermia information: Refer to State of Alaska Injuries Guidelines by searching for-- State of Alaska Cold Injuries, it will show up usually as the first choice. Open the link and the Cold Injuries PDF will appear, it should be the 2014 Guidelines.
Reference Gordon Giesbrecht PhD video-Cold Water Boot Camp . View the video or the 10 minute presentation for 1-10-1 Rules and other information. This video is also on the State of Alaska’s Office of Safe Boating website: www.dnr.alaska.gov/parks/boating
State of Alaska’s Office of Safe Boating (Publications) has numerous videos, clips and links to YouTube clips on hypothermia-- http://dnr.alaska.gov/parks/boating/index
Understand that if you fall into cold water you need to get out of it. Self Rescue is possible for a limited time. You need to attraction attention by using signaling devices (whistles, mirrors, horns etc., will work).

## Slide 15: Cold Water Survival
Practice:
  Re-boarding techniques
  MAYDAY calls
  Conduct overboard drills using an object to simulate a person in the water.

## Slide 16: Signaling Devices
Vessels less than 39 feet, four inches (12 meters) are not specifically required to carry a sound-producing device, such as a whistle or horn, but must have some means of making an “efficient sound signal.” Fastening a whistle to each PFD is a great way to meet this requirement.
Vessels over 39 feet, four inches (12 meters) are required to carry a whistle or horn.
Notes: Signaling Devices
Vessels less than 39 feet, four inches (12 meters) are not specifically required to carry a sound-producing device, such as a whistle or horn, but must have some means of making an “efficient sound signal.” Fastening a whistle to each PFD is a great way to meet this requirement.
• Vessels over 39 feet, four inches (12 meters) are required to carry a whistle or horn.

## Slide 17
MSD holds sewage
Some MSDs can treat sewage
Use pump out stations, if available
Alaska waters within three miles of shore are no discharge zones.
Type I and II marine Heads must be sealed to prevent discharge
>>
17
Marine Sanitation
Devices (MSD)
Notes: MARINE SANITATION DEVICES
Motorboats with marine toilets are not allowed on public waters unless the toilet is equipped with a Type I, II or III marine sanitation device (MSD.) Type I and II MSDs chemically treat sewage. Type III MSDs are holding tanks for raw sewage.
Raw sewage shall not be discharged in any public waters. Type I and II MSDs must be sealed or locked while the vessel is on “no discharge” waters.

## Slide 18
International Marine Pollution Law
Notes: No trash, garbage or waste overboard in waters of USA. This or similarly worded decal is to be applied to boats 26 feet and longer as reminder to not pollute. Applies to all boaters.

## Slide 19: Diving/Snorkeling Flags
Boaters remain 100 feet away
Divers within 100 feet of diver flag
Divers shall not obstruct boat traffic
Top of 3 feet or more above water
Notes: Diving/Snorkeling Flags
“Diver down flag” shall be a red field of not less than 10 inches x 10 inches dimension with a white diagonal stripe not less than 1-1/2 inches wide running upper left to lower right. The flag shall be displayed at all times and be affixed to a separate flotation device. No such flag shall be attached to any navigational device or placed so as to obstruct boat traffic. Divers must come up within 100 feet of flag. All powerboats will remain a minimum distance of 100 feet away from the marker flag. The top of the flag shall be at least 3 feet above the surface of the water.
Navigation Rules and Regulations regarding diving operations.
Alfa Flag. Whenever the size of the vessel engaged in diving operations makes it impractical to exhibit all lights and shapes prescribed in paragraph (d) of Rule 27, as appropriate, the following instead shall be exhibited:
1. at night - three all-around lights in a vertical line where they can best be scene. The highest and lowest of these lights shall be red and the middle light shall be white.
2. daylight - a rigid replica of the International Code flag “A” not less than 1 meter in height. measures shall be taken to ensure its all-round visibility.
The “A” flag is a navigation signal indicating the vessel’s restricted maneuverability and does not pertain to the location of the diver.

## Slide 20: Oil/Fuel Spills
Spills reported immediately to:
US Coast Guard at 1-800-424-8802
Placard displayed for vessels 26 feet and longer’
Notes: Waste and Trash, continued
The discharge of oil and hazardous substances is strictly prohibited by the regulations issued under the Federal Water Pollution Control Act. This act requires all boats with propulsion machinery to have a capacity to retain oil mixtures onboard.
You are not allowed to discharge oil or hazardous substances.
You are not allowed to sump oil into the bilge of the boat without means for proper disposal.
You must discharge oil wastes to a reception facility.
On recreational boats a bailer or bucket is adequate.
You must immediately notify the U.S. Coast Guard if your boat discharges oil or hazardous substances in the water. Call toll free 1-800-424-8802. Report the discharge’s location, color, source, substances, size and time observed.
If your boat is 26’ or longer you must display a 5” x 8” placard made of durable material fixed in a conspicuous place in the machinery spaces, or at the bilge pump control station stating the following:

## Slide 21: Boating Accident Reporting
Stop, render aid and provide contact information
Report required when –
1. Death or personal injury requiring medical treatment beyond first aid
2. Damage to property in excess of $500.
Loss of life-report within 48 hours, otherwise within 10 days
Notes: AK Accident Reports.
The operator of any vessel involved in a collision, accident, or other casualty has a duty to render aid to others that were involved or affected by the collision or accident if they can do so without serious damage to his or her own vessel, crew or passengers. The aid rendered should be that which may be practicable and necessary in order to save them from or minimize any danger caused by the incident.
The operator of any vessel involved must provide his or her name, address, and vessel registration to any person who was injured during the incident and to the owner of any property damaged by the incident.
The operator of any vessel involved in a collision, accident, or other casualty which results in death or personal injury that requires medical treatment beyond first aid, or damage to property in excess of five hundred dollars ($500) must file a full description of the incident.
An accident report in a case involving a loss of life must be submitted to the Alaska Office of Boating Safety 550 West 7th Avenue, Suite 1380
Anchorage, AK 99501
within forty-eight (48) hours of the incident.
An accident report in a case involving a reportable injury or property damage as described above must be submitted to the Department within ten (10) days of the incident.
An accident report must be submitted in person or by mail to the Alaska Office of Boating Safety

## Slide 22: Boating Accident Reporting
Mail TO:
Alaska Office of Boating Safety
550 West 7th Avenue, Suite 1380
Anchorage, AK 99501
Fax to:
(907) 269-8907
Email to:
officeofboatingsafety@alaska.gov
Notes: Accident Reports.
File a full description of the incident with the Alaska office of Boating Safety 550 West 7th Avenue, Suite 1380 Anchorage, AK 99501
..

## Slide 23: Alaska Contacts
Alaska Boating Safety Program (907) 269-8706 www.alaskaboatingsafety.org
Alaska Water Wise Courses (907) 269-8704 www.alaskaboatingsafety.org
Alaska Marine Safety Education Association (907) 747-3287 www.amsea.org
Knik Canoers and Kayakers, www.kck.org
Fairbanks Paddlers, www.fairbankspaddlers.org
Notes: Alaska Boating Safety Program (907) 269-8706 www.alaskaboatingsafety.org
Alaska Water Wise Courses (907) 269-8704 www.alaskaboatingsafety.org
Alaska Marine Safety Education Association (907) 747-3287 www.amsea.org
Knik Canoers and Kayakers, www.kck.org
Fairbanks Paddlers, www.fairbankspaddlers.org

## Slide 24: Thank you!
Any questions?
Find other Auxiliary boating courses at http://www.cgaux.org/boatinged
Request a vessel safety check at http://www.safetyseal.net
Learn more about joining the Auxiliary at: http://join.cgaux.org