## Slide 1: Iowa Supplement
For use with Boat America and Boating Skills & Seamanship

## Slide 2: Boating References
Material for this supplement is contained in the publication:
“The Handbook of Iowa Boating Laws
and Responsibilities”
downloadable at:
https://www.boat-ed.com/assets/pdf/handbook/ia_handbook_entire.pdf
Notes: Material for this power point program was sourced from the this reference. The final examination includes a ten-question Iowa supplemental assessment of learning regulations discussed in this section.

## Slide 3: Mandatory Education
A person under 12 years of age may operate a vessel propelled by a motor of more than 10 horsepower, including a personal watercraft, only if he or she is accompanied on board by a responsible person who is at least 18 years old and experienced in operating the vessel.

## Slide 4: Mandatory Education
A person 12 years of age or older but younger than 18 years of age may operate a vessel propelled by a motor of more than 10 horsepower, including a personal watercraft, only if he or she has successfully completed a boater education course approved by the Iowa Department of Natural Resources, or is accompanied on board by a responsible person who is at least 18 years old and experienced in operating the boat.

## Slide 5: Mandatory Education
Persons required to have successfully completed a boater education course must carry their boater education certificate on board and make it available upon request by an enforcement officer.

## Slide 6: Boating Accidents
An operator involved in a boating accident must stop his or her vessel immediately at the scene of the accident and assist anyone injured or in danger from the accident, unless doing so would seriously endanger his or her own vessel or passengers.

## Slide 7: Reporting Accidents
Accidents must be reported in writing to the Iowa Department of Natural Resources (DNR) within 48 hours of the accident in cases resulting in death, disappearance, or personal injury requiring medical treatment.
Accidents must be reported in writing to the DNR within five days if damage to vessel or other property exceeds $2,000.

## Slide 8: Vessel Registration
An Iowa Registration Certificate is required to operate on Iowa’s public waters. Exceptions are:
  Inflatable vessels 7 feet or less with no motor or sail;
  Canoes and kayaks 13 feet or less with no motor or sail;
  Vessels registered in another state and using Iowa waters for 60 days or less in a calendar year.
• The registration certificate (pocket-sized) must be on
board and available for inspection by an
enforcement officer.

## Slide 9: Vessel Registration
Registration number and decals must be displayed as follows:
  Number must be painted, applied as a decal, or otherwise affixed to the forward half of each side;
  No other numbers may be displayed on either side of the bow;
  Number is read from left to right on both sides;
  Number must be at least 3-inch-high BLOCK letters;
  Number’s color must contrast with the background.

## Slide 10: Vessel Registration
The passenger capacity of a vessel must be painted on or attached to the starboard (right) side of the vessel within 9 inches of the transom clearly visible above the waterline when the vessel is fully loaded.
Displayed passenger capacity must match the passenger capacity on the Registration Certificate.
If the vessel does not have a capacity plate, the capacity is the “operator’s responsibility,” and the letters OR must be on the Registration Certificate and displayed on the vessel instead of a capacity number.
The capacity number or OR must be the same size as the registration numbers on the bow.

## Slide 11
Correct Display of Numbers
3’’ High
Contrasting colors
Decal toward stern within 4 inches of number
IA 2345 AB
IA 2345 AB
Port Side
Starboard Side
Notes: Display of numerals and decals on vessel.
1. The number awarded, exactly as shown on the certificate of numerals shall be painted on, or attached to, each side of the bow of the vessel for which it was issued.
2. The numerals shall be placed on each side of the forward half of the vessel in such position as to provide clear legibility for identification. The numerals shall read from left to right and shall be in block characters of good proportion not less than three inches in height. The numerals shall be of a color which will contrast with the background, and so maintained as to be clearly visible and legible; i.e., dark numerals on a light background or light numerals on a dark
background.

## Slide 12: Capacity Number
Capacity number toward stern within 9 inches of transom
Starboard Side

## Slide 13: Maximum Capacities
Capacity label by manufacturer
Number of persons
Weight for persons, motor and gear
Maximum engine horsepower
Notes: Overloading. Never overload your boat with passengers or cargo beyond its safe carrying capacity. Capacity labels are required on all vessels less than 20 feet manufactured after1972, and are affixed by the manufacturer. Iowa law forbids altering, defacing or removing the plate.
No vessel may be loaded with passengers or cargo beyond its safe cargo carrying capacity.
The maximum persons capacity marked on a vessel's maximum capacities plate must not be exceeded.
The maximum weight capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard Maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe loading requirements.
Overpowering
No vessel may be operated beyond its safe powering capacity.
The maximum horsepower capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard Maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe powering requirements.

## Slide 14: Life Jackets
Children under 13 years of age must wear a properly sized and fitted PFD when the boat is underway on any Iowa waters, unless the child is below deck, in an enclosed cabin, or is a passenger on a commercial vessel with a capacity of twenty-five persons or more

## Slide 15: Life Jackets
All vessels must have at least one USCG approved wearable Type I, II, III or V life jacket for each person on board.
In addition, one USCG approved throwable Type IV must be on board vessels 16 feet or longer except canoes or kayaks.

## Slide 16: Life Jackets
Each person on board a personal watercraft (PWC) or being towed behind a vessel on water skis, surfboard, or similar device must wear a USCG approved Type I, II, III, or V life jacket.
Inflatable life jackets are not approved for persons on PWCs or being towed.
Stand-Up Paddleboards (SUP) are not required to wear a life jacket but must have one on board.

## Slide 17: Marine Toilets
All recreational boats with installed toilet facilities must have an operable marine sanitation device on board. All installed marine sanitation devices (MSD) must be Coast Guard certified.
Vessels 65 feet or less may use a Type I, II or III MSD.
Vessels over 65 feet must install a Type II or III MSD.

## Slide 18: Marine Toilets
When operating a vessel on a body of water where the discharge of treated or untreated sewage is prohibited the operator must secure the device in a manner which prevents any discharge.
Some acceptable methods are: padlocking overboard discharge valves in the closed position, using non releasable wire tie to hold overboard discharge valves in the closed position, closing overboard discharge valves and removing the handle, locking the door, with padlock or key lock, to the space enclosing the toilets (for Type I and Type II only).

## Slide 19
International Marine Pollution Law
Notes: MARPOL Regulations:
All vessels must obey MARPOL regulations developed in the 1970s, revised in 2006 and guidelines accepted in 2012 to protect the marine environment from operational pollution.
The U.S. legislation that implements MARPOL Annex V, bans the dumping of specified garbage and all plastics in all navigable waters of the United States. (It is illegal to discard fishing line on land or in state waters.) It also places restrictions on the disposal of other types of shipboard solid wastes. Vessels over 26 feet must display a durable placard explaining MARPOL Annex V disposal regulations..

## Slide 20: Oil/Fuel Spills
Spills reported immediately to;
US Coast Guard at 1-800-424-8802
Placard displayed for vessels 26 feet and longer’
Notes: Waste and Trash, continued
The discharge of oil and hazardous substances is strictly prohibited by the regulations issued under the Federal Water Pollution Control Act. This act requires all boats with propulsion machinery to have a capacity to retain oil mixtures onboard.
You are not allowed to discharge oil or hazardous substances.
You are not allowed to sump oil into the bilge of the boat without means for proper disposal.
You must discharge oil wastes to a reception facility.
On recreational boats a bailer or bucket is adequate.
You must immediately notify the U.S. Coast Guard if your boat discharges oil or hazardous substances in the water. Call toll free 1-800-424-8802. Report the discharge’s location, color, source, substances, size and time observed.
If your boat is 26’ or longer you must display a 5” x 8” placard made of durable material fixed in a conspicuous place in the machinery spaces, or at the bilge pump control station stating the following:

## Slide 21: Aquatic Invasive Species
Trailer boaters should remove visible mud, plants, fish or animals from boats and trailers prior to transport to another body of water.
Scrape any mussels from boat or outdrive, and flush hull, bilges & water holding compartments with hot water (use 1 quart / gal of vinegar).
Do not release plants or fish, including bait, into a body of water unless it came from same body of water.
Illegal transport of invasive species is subject to a $500 fine.
To prevent the spread of non-native fish and mollusks in our waterways, boaters should follow these simple rules:
Notes: MARINE AQUATIC INVASIVE SPECIES
If a vessel sits at a dock for too long, growth can occur on the hull. Invasive species can also collect in bilge areas, live wells, or other places that may collect water. If a vessel moves between seasonal ports, the introduction of an AIS may occur. Many of the fouling species that grow on vessel hulls exist because they are invasive and have no predators. Often the introductions are from ballast water taken on in foreign waters and discharged in US waters. Steps are being taken nationally to minimize these introductions. Local boaters can help by removing the species on their boats and trailers and properly preparing and maintaining their boat’s bottom.
Non-native aquatic plants or animals are also known as nuisance or aquatic invasive species (AIS). These species tend to grow at a rate such that they can displace beneficial native species, disrupt the ecosystem and drastically reduce recreational activities, including swimming. Please prevent new introductions of invasive plants and animals: Clean, Drain, Dry your boat and gear
FRESHWATER
Plant species such as Eurasian milfoil, variable leaf milfoil and fanwort have been introduced into Louisiana’s lakes and ponds, and can impact the ecosystem and reduce recreational activities. Invasive plants can form a dense mat just below the water’s surface, which interferes with boating, swimming and other recreational activities.
1. Eurasian milfoil: Submerged, perennial aquatic plant with green feathered type leaves. The stems are brownish-red to light green. Milfoil produces pink flowers between July and August.
2. Fanwort: Submerged plant that ranges in color from grass green to olive and to reddish brown. The leaves are finely divided and strictly opposite arranged. Small white flowers with six petals emerge among the floating leaves.
3. Zebra mussel: Zebra mussels are small, striped rigid mussel that grows to a maximum length of 2.5 cm(approximately one inch)in length. The shell color is black or brown with variable white to yellow striped or zig zag patterns and they can live up to five years. These mussels can impact the ecosystem, foul boat hulls and engine cooling systems, are sharp to step on and can clog power plant, industrial and drinking water intakes.
4. Quagga mussel: The quagga is slightly larger than the zebra mussel. The shell is striped but is more pale toward the end of the hinge. Color patterns vary widely with black, cream, or white bands. The quagga has a rounded angle and a convex ventral side.
5. Chinese mitten crab: The claws are of equal size and appear “furry” with whitish tips. The smooth shell is brown to green with four spines (the fourth can be small) on each side. There is a notch between the eyes. This crab reproduces in saltwater but spends most of its life in freshwater.
6. New Zealand mud snails: Relatively small snail that has brown or black cone shaped shell with seven to eight whorls. Between the whorls are deep grooves. This snail has the ability to reproduce quickly and populations can rapidly reach high densities under suitable conditions.
7. Rusty crayfish: A large crayfish with reddish spots on each side of the body just in front of the tail, grayish green color, smooth mandibles (mouthparts without serrated edge) and black bands on tips of claws. Rusty crayfish are aggressive and can displace native crayfish. They feed heavily on invertebrates that are important food sources for fishes and can destroy aquatic vegetation beds, impacting habitat used by other invertebrates and game fish. Rusty crayfish are often spread via bait buckets.
8. Asian clam: A bivalve that can grow as large as 5 cm (2 inches)wide and live up to seven years. Asian clams can be identified by the presence of yellow and brown color concentric rings on their shell. The outer side of the shell can flake, revealing white spots. Asian clam excretions encourage algal growth which reduces water quality for native flora and fauna.
Asian clams can aggressively colonize the bottom of waterways and can outcompete native species for space.

## Slide 22: Towing Skiers
Every vessel towing a person on water skis, surfboard, or other device must have on board, in addition to the operator, a responsible person to observe the towed person.
All persons being towed must wear a USCG approved life jacket. Inflatables are not approved for people being towed.

## Slide 23: Towing Skiers
A boat towing a person may do so between sunrise and one half hour after sunset only.
  A PWC may tow a person only between sunrise and sunset.
  A person may not operate a vessel if its capacity would be exceeded by the persons in the vessel plus the person towed.
  A PWC must be rated for three people including the observer.
  Exceptions exist for exhibitions authorized by the DNR.

## Slide 24: Diving/Snorkeling Flags
Divers and snorkelers must display a diver-down flag.
Vessels not engaged in diving must stay 50 feet away from the flag.
Notes: Diving and Underwater Operations. Scuba divers or snorkelers must display a diver-down flag that marks their diving area. Vessels should remain at least 100 feet away from the flag. The blue/white ALPHA flag at least 3.3 feet (one meter) high and visible from all directions is also used to show underwater operations from a vessel in federal waters. It may be used in addition to the state’s diver down flag. Boaters must not come within 100 feet of the dive flag.

## Slide 25: Unlawful Operation
In Iowa it is illegal to:
  Reckless or negligent operation of a vessel or the reckless manipulation of water skis, surfboard, or similar device that causes danger to life, limb, or property.
  To operate a vessel at greater than 5 miles an hour in any posted “no wake zone.”
  To operate at greater than 5 mph within 100 feet of another vessel underway at 5 mph or less.

## Slide 26: Unlawful Operation
In Iowa it is illegal to:
  To operate at greater than 10 mph unless vision in unobstructed for at least 200 feet ahead.
  To operate at greater than 10 mph within 300 feet of shore (except in specially zones areas) on any lake or federal impoundment.
  To operate at greater than 5mph within 300 feet of shore on any lake in Dickinson County.

## Slide 27: Unlawful Operation
In Iowa it is illegal to:
  To operate at greater than 25 mph between one-half hour after sunset and sunrise on any lake in Dickinson County.
  Operate at greater than 10 mph between one hour after sunset and one hour before sunrise on Lake Delhi.
  Overloading the vessel with more passengers than the capacity plate permits.

## Slide 28: Unlawful Operation
In Iowa it is illegal to:
  Overpower the vessel beyond the recommended horsepower shown on the capacity plate.
  Interfere with search and rescue operations being conducted.
  Leaving vessel unattended tied or moored to a dock adjacent to a public boat launching ramp or dock posted for loading and unloading.

## Slide 29: Intoxication
Iowa law prohibits boating while intoxicated (BWI). This includes the operation of any vessel or manipulation of any water skis, surfboard, or similar device while under the influence of alcohol, marijuana, a narcotic, hypnotic, or other drug, or any combination of substances.

## Slide 30: Intoxication
A person is considered to be intoxicated if he or she:
• Has a blood, breath, or urine concentration of 0.08%; or
Has any amount of a controlled substance present in his or her person, as measured in blood or urine.

## Slide 31: Intoxication
Iowa law includes the following penalties for BWI:
  First conviction a fine up to $1000, jailed for at east 48 hours, and prohibited from operating a vessel for one year.
  Second conviction a fine up to $5000, jailed for 7 days, and prohibited from operating a vessel for two years.
  Third and subsequent convictions, a fine up to $7500, jailed for up to one year, and prohibited from operating a vessel for 6 years.

## Slide 32: Intoxication
Persons convicted of BWI will also be assigned to substance abuse evaluation/treatment and must attend a course for drinking drivers.
By operating a vessel on Iowa waters, you have given implied consent for law enforcement officers to test you to detect the possible presence of alcohol or drugs.

## Slide 33: Personal Watercraft
Persons under 12 years of age may operate a PWC only if accompanied on board by a responsible person at least 18 years old and experienced in operating a PWC.
Persons 12 years old but younger than 18 may operate a PWC only if he or she has completed successfully an approved boater safety class or is accompanied on board by a responsible person at least 18 years old and experienced in operating a PWC.
Notes: Remind students that PWCs refer to what they probably think of as Jet Skis. Jet Ski is a trademark of Kawasaki.

## Slide 34: Personal Watercraft
Each person riding a PWC must wear a U.S. Coast Guard approved type I, II, II, or V life jacket.
A safety lanyard must be attached to his or her person, clothing, or life jacket.
PWCs may not operate between sunset and sunrise.
Illegal to chase or harass wildlife.
Illegal to operate at greater than 5 miles per hour in posted “no wake zone.”
.
Notes: Remind students that PWCs refer to what they probably think of as Jet Skis. Jet Ski is a trademark of Kawasaki.

## Slide 35: Personal Watercraft
Illegal to operate at greater than 5 mph within 100 feet of another vessel that is underway at 5 mph or less.
Illegal to operate at greater than 5 mph within 50 feet of another vessel that is underway at greater than 5 mph.
Illegal to operate at greater than 10 mph unless vision is unobstructed for at least 200 feet ahead.
Illegal to operate at greater than 10 mph within 300 feet of shore.

## Slide 36: Thank you!
Any questions?
Find other Auxiliary boating courses at http://www.cgaux.org/boatinged
Request a vessel safety check at http://www.safetyseal.net
Learn more about joining the Auxiliary at: http://join.cgaux.org