## Slide 1: Kentucky Supplement
For use with Boat America and Boating Skills & Seamanship

## Slide 2: Boating References
Kentucky Fishing & Boating Guide
http://fw.ky.gov/Boat/Pages/default.aspx
Notes: The final examination includes a ten-question Kentucky supplemental assessment of learning regulations discussed in this section.
Some definitions:
No Wake Speed - a vessel may not operate in excess of the idling speed or the slowest possible speed necessary to maintain steerage under prevailing wind and water conditions.
No Wake Speed Zone - an area restricting motorboats from attaining a speed which would produce a wake that would noticeably disturb other motorboats or vessels, docks, piers, or any other shoreline facility within the designated area. This area should be marked by REGULATORY BOUYS or signs bearing the words ‘No Wake’.
Personal Watercraft or PWC - means a small Class A vessel which uses an outboard motor or an inboard motor powering a water jet pump as its primary source of motive power and which is designed to be operated by a person sitting, standing, or kneeling on, or being towed behind the vessel rather than the conventional manner of sitting or standing inside the vessel designed area.
Motorboats Which Carry Passengers for Hire Requirements
Motorboats which carry passengers for hire must be provisioned with a Type I personal floatation device for each person carried. They must also be provisioned with an additional number of Type I personal floatation devices suitable for children equal to at least ten percent (10%) of the maximum number of persons carried, unless the service is such that children are never carried. All personal floatation devices must be Coast Guard approved (see Personal Flotation Devices), must be maintained in a good and serviceable condition, and must be readily available for use at all times.
Motorboats carrying passengers for hire must be operated and navigated by a person duly licensed by the United States Coast Guard. This provision does not apply to whitewater outfitters and guides licensed under Kentucky Code, chapter twenty, article two [§20-2-23(a)] nor boating and canoeing outfitters and guides licensed under Kentucky Code, chapter twenty, article two [§20-2-26].
Motorboats carrying more than six (6) passengers must be inspected and certified by the United States Coast Guard.

## Slide 3: Boater Education
To operate a motorboat with an engine of more than 10 hp on Kentucky waters the operator must be 12 years of age or older:
Operators 12 to 17 years old (including PWCs) must have passed a NASBLA approved boating safety course and carry their boater safety education certificate on board.
Or be accompanied by a person 18 years of age or older or by a person who possesses a boater education card.
Notes: Who May operate a vessel in Kentucky?—
A person must be 12 years or older to operate a motorboat (including PWC) 10 hp or over on Kentucky public waters.
Operators 12 to 17 years of age may legally operate a motorized vessel over 10 horsepower (including personal watercraft) only if they:
Have passed a NABLA-approved boating safety course and carry on board their boater education certificate or…
Are accompanied on board by a person 18 years old or older or by a person who possesses a boater education card.
Enforcement
Kentucky law enforcement officers patrol the waterways to make your boating experience safe and pleasant. Cooperate with them by following the laws and guidelines.
Carry the Card: Vessel operators who are required to have a Boater Education Card must carry the card on board the vessel and have it available for inspection by an enforcement officer.
Penalty: Not carrying your Boater Education Card when one is required can result in a fine.

## Slide 4: Law Enforcement
Kentucky law enforcement officers patrol the waterways.
Vessel operators who are required to have a Boater Education Card must carry the card on board the vessel and have it available for inspection by an enforcement officer.
Penalty: Not carrying a Boater Education Card when one is required can result in a fine.
Notes: Who May operate a vessel in Kentucky?—
A person must be 12 years or older to operate a motorboat (including PWC) 10 hp or over on Kentucky public waters.
Operators 12 to 17 years of age may legally operate a motorized vessel over 10 horsepower (including personal watercraft) only if they:
Have passed an approved boating safety course and carry on board their boater education certificate or…
Are accompanied on board by a person 18 years old or older or by a person who possesses a boater education card.
Enforcement
Kentucky law enforcement officers patrol the waterways to make your boating experience safe and pleasant. Cooperate with them by following the laws and guidelines.
Carry the Card: Vessel operators who are required to have a Boater Education Card must carry the card on board the vessel and have it available for inspection by an enforcement officer.
Penalty: Not carrying your Boater Education Card when one is required can result in a fine.

## Slide 5: Boat Registration
Mechanically propelled boats must be registered with the Kentucky DFWR at the county clerk’s office.
One year fee dependent on boat length.
Registration certificate must be on board.
8 digit number with validation decal
KY 2345 AB (decal) or
KY-2345-AB (decal)
Notes: Class A Vessels (less than 16’ in length) $19.00
Class 1 Vessels (16’ to less than 26’ in length) $23.00
Class 2 Vessels (26’ to less than 40’ in length) $29.00
Class 3 Vessels (over 40’ in length) $33.00
Inboard boats (regardless of size) $34.00
Boats propelled by an electric (trolling) motor only $9.00
Registration Requirements.
All mechanically powered vessels used primarily in this state must have a Kentucky registration. Boats are registered at the county clerk’s office. Persons may register in the county of their residence or the county of principal use. Boat registrations expire April 30 each year. Boats registered in other states may be used for up to 60 consecutive days in Kentucky without registering here. All boats operated in Kentucky must have the registration certificate on board. Boats that are rented from a marina or boat livery must have a lease agreement on board.

## Slide 6
Correct Display of Numbers
3’’ High
Contrasting colors
Sticker within 6 inches toward aft in line of KY Number
KY 2345 AB
KY 2345 AB
Port Side
Starboard Side
Notes: Display of numerals and decals on vessel.
1. The number awarded, exactly as shown on the certificate of numerals shall be painted on, or attached to, each side of the bow of the vessel for which it was issued.
2. The numerals shall be placed on each side of the forward half of the vessel in such position as to provide clear legibility for identification. The numerals shall read from left to right and shall be in block characters of good proportion not less than three inches in height. The numerals shall be of a color which will contrast with the background, and so maintained as to be clearly visible and legible; i.e., dark numerals on a light background or light numerals on a dark
background.
3. The commissioner will furnish to all applicants two (2) decals bearing the numbers of the year of expiration, which will establish valid registration. The decals are to be displayed on each side of the boat (within 6 inches) toward aft of the assigned Kentucky number.
(decal) KY1234 AB or KY-1234-AB (decal)

## Slide 7: Maximum Capacities
7
Capacity label by manufacturer
Number of persons
Weight for persons, motor and gear
Maximum engine horsepower
Copyright 2018 Coast Guard Auxiliary Association
Notes: Overloading and Overpowering.
No vessel may be loaded with passengers or cargo beyond its safe cargo carrying capacity.
The maximum persons capacity marked on a vessel's maximum capacities plate must not be exceeded.
The maximum weight capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard Maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe loading requirements.
Overpowering
No vessel may be operated beyond its safe powering capacity.
The maximum horsepower capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard Maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe powering requirements.

## Slide 8: Life Jackets
A USCG approved wearable personal flotation device (PFD) correctly sized and in serviceable condition is required to be on board for every person
Boats 16 feet and longer must additionally carry a USCG approved throwable device (not canoe or kayak)
Persons being towed, those 12 and under, and those aboard a PWC MUST wear a PFD
PFDs with water impact ratings are suggested for high speed watersports such as operating PWC and being towed
Notes: KY Personal Flotation Devices (PFD)
All vessels, except sailboards, must carry one wearable U.S. Coast Guard-approved Type I, II, III, or V PFD for each person on board.
Ion addition, vessels 16 feet in length or longer must have one U.S. Coast Guard-approved Type IV PF on board and readily accessible.
Children under 12 years of age must wear a U.S. Coast Guard-approved.Type I, II, III, PFD at all times while underway on the open deck of any vessel.
A person under 16 years of age must wear a U.S. Coast Guard-approved.Type I, II, III, PFD at all times when aboard a sailboard.
Everyone on board a PWC must wear a U.S. Coast Guard-approved.Type I, II, III, PFD.
Anyone being towed behind a vessel must wear a U.S. Coast Guard-approved.Type I, II, III, PFD.

## Slide 9: Water Skis & Surfboards
Applies to persons being towed
All being towed must wear PFD
Allowed only between sunrise and sunset
The towing boat must have 12 year or older observer or a wide angle rear view mirror.
Notes: KY Water Skis and Surfboards
While this section is titled waterskiing, it applies to persons being towed on any device such as knee boards, inner tubes, etc. Water-skiing is only allowed between sunrise and sunset. Additionally, it is illegal to manipulate skis, surfboards, etc. while intoxicated or under the influence of any other substance that impairs one’s operating ability. Both the operator and skier should be alert to the areas of a lake or river marked as “no ski.” Persons shall not ski within 100 feet of a commercial boat dock, a moorage harbor or a swimming area or within 2,000 feet of a lock or dam. Skiers who ski too close to other boats, docks and obstructions are showing poor judgement. Many of the complaints officers receive while patrolling the water are those about skiers skiing too close.
Persons being towed on any device must wear a Type I, II or III PFD.
Boats (including personal watercraft) towing skiers must have, in addition to the operator of the boat, an observer 12 years of age or older or a wide angle rearview mirror mounted so that the operator can check on the skier but still give full attention to traffic ahead.
There must be adequate seating for all riders.
Boats towing kites and similar airborne devices must:
• Have, in addition to the operator, an observer 12 years or older (mirror will not suffice),
• Stay 500 feet from commercial docks and ramps,
• Limit the tow rope to 150 feet or less,
• Have no more than two persons being towed.

## Slide 10: Water Skis & Surfboards
Illegal to tow while intoxicated
Stay clear of no ski zones –
  No towing within 100 feet of commercial boat dock, moorage harbor, swim area
  None within 2000 feet of lock or dam
Notes: KY Water Skis and Surfboards
While this section is titled waterskiing, it applies to persons being towed on any device such as knee boards, inner tubes, etc. Water-skiing is only allowed between sunrise and sunset. Additionally, it is illegal to manipulate skis, surfboards, etc. while intoxicated or under the influence of any other substance that impairs one’s operating ability. Both the operator and skier should be alert to the areas of a lake or river marked as “no ski.” Persons shall not ski within 100 feet of a commercial boat dock, a moorage harbor or a swimming area or within 2,000 feet of a lock or dam. Skiers who ski too close to other boats, docks and obstructions are showing poor judgement. Many of the complaints officers receive while patrolling the water are those about skiers skiing too close.
Persons being towed on any device must wear a Type I, II or III PFD.
Boats (including personal watercraft) towing skiers must have, in addition to the operator of the boat, an observer 12 years of age or older or a wide angle rearview mirror mounted so that the operator can check on the skier but still give full attention to traffic ahead.
There must be adequate seating for all riders.
Boats towing kites and similar airborne devices must:
• Have, in addition to the operator, an observer 12 years or older (mirror will not suffice),
• Stay 500 feet from commercial docks and ramps,
• Limit the tow rope to 150 feet or less,
• Have no more than two persons being towed.

## Slide 11: Signaling Devices
Mouth whistle or powered horn or whistle audible for one-half mile required for
boats less than 65.6 feet, including PWCs.
Boats greater than 65.5 feet require above plus a bell.
Notes: Signaling Devices

## Slide 12
MSD holds sewage
Some MSDs can treat sewage
Use pump out stations
ALL Kentucky waters are no discharge zones.
Type I and II marine Heads must be sealed to prevent discharge
>>
12
Marine Sanitation
Devices (MSD)
Notes: MARINE SANITATION DEVICES
Motorboats with marine toilets are not allowed on public waters unless the toilet is equipped with a Type I, II or III marine sanitation device (MSD.) Type I and II MSDs chemically treat sewage. Type III MSDs are holding tanks for raw sewage.
Raw sewage shall not be discharged in any public waters. Type I and II MSDs must be sealed or locked while the vessel is on “no discharge” waters.

## Slide 13
International Marine Pollution Law
Notes: No trash, garbage or waste overboard in waters of USA. This or similarly worded decal is to be applied to boats 26 feet and longer as reminder to not pollute. Applies to all boaters.

## Slide 14: Diving/Snorkeling Flags
Boaters remain 100 feet away
Divers within 100 feet of diver flag
Divers shall not obstruct boat traffic
Top of 3 feet or more above water
Notes: Diving/Snorkeling Flags
“Diver down flag” shall be a red field of not less than 10 inches x 10 inches dimension with a white diagonal stripe not less than 1-1/2 inches wide running upper left to lower right. The flag shall be displayed at all times and be affixed to a separate flotation device. No such flag shall be attached to any navigational device or placed so as to obstruct boat traffic. Divers must come up within 100 feet of flag. All powerboats will remain a minimum distance of 100 feet away from the marker flag. The top of the flag shall be at least 3 feet above the surface of the water.
Navigation Rules and Regulations regarding diving operations.
Alfa Flag. Whenever the size of the vessel engaged in diving operations makes it impractical to exhibit all lights and shapes prescribed in paragraph (d) of Rule 27, as appropriate, the following instead shall be exhibited:
1. at night - three all-around lights in a vertical line where they can best be scene. The highest and lowest of these lights shall be red and the middle light shall be white.
2. daylight - a rigid replica of the International Code flag “A” not less than 1 meter in height. Measures shall be taken to ensure its all-round visibility.
The “A” flag is a navigation signal indicating the vessel’s restricted maneuverability and does not pertain to the location of the diver.
SKIN AND SCUBA DIVING (301 KAR 1:410, 6:030)
Skin or SCUBA diving is prohibited in all lakes owned or managed by the Kentucky Department of Fish and Wildlife Resources, except during emergencies, on Greenbo Lake and during salvage operations when the diver has written permission from the regional director or local wildlife and boating law enforcement officer assigned to the specific body of water in which the diving is to take place.
Persons diving or submerging with the aid of a mechanical breathing apparatus in an area where boats might be are required by law to display the diver’s flag.
This flag should be put on a buoy, boat or other floating platform so boaters will readily see it. Approaching boats must stay outside of a 100-foot radius of the flag. Divers must surface within a 50-foot radius unless there is an emergency.
Divers shall not dive in established traffic lanes nor interfere with anyone fishing unless emergency operations are in progress.

## Slide 15: Oil/Fuel Spills
Spills reported immediately to;
US Coast Guard at 1-800-424-8802
Placard displayed for vessels 26 feet and longer’
Notes: Waste and Trash, continued
The discharge of oil and hazardous substances is strictly prohibited by the regulations issued under the Federal Water Pollution Control Act. This act requires all boats with propulsion machinery to have a capacity to retain oil mixtures onboard.
You are not allowed to discharge oil or hazardous substances.
You are not allowed to sump oil into the bilge of the boat without means for proper disposal.
You must discharge oil wastes to a reception facility.
On recreational boats a bailer or bucket is adequate.
You must immediately notify the U.S. Coast Guard if your boat discharges oil or hazardous substances in the water. Call toll free 1-800-424-8802. Report the discharge’s location, color, source, substances, size and time observed.
If your boat is 26’ or longer you must display a 5” x 8” placard made of durable material fixed in a conspicuous place in the machinery spaces, or at the bilge pump control station stating the following:

## Slide 16: Aquatic Invasive Species
Trailer boaters should remove visible mud, plants, fish or animals from boats and trailers prior to transport to another body of water.
Scrape any mussels from boat or outdrive, and flush hull, bilges & water holding compartments with hot water (use 1 quart / gal of vinegar).
Do not release plants or fish, including bait, into a body of water unless it came from same body of water.
To prevent the spread of non-native fish and mollusks in our waterways, boaters should follow these simple rules:
Notes: KY Aquatic Nuisances
Introducing non-native species into Kentucky waters can upset the balance of the ecosystem., harming the environment. Some common nuisance species found in Kentucky include Asian carp, hydrilla, and zebra mussel:
Asian Carp-Two species of Asian carp, the big head and silver, have invaded river systems in Kentucky. Any river or large stream tributary to the Ohio or Mississippi Rivers most likely possess Asian carp. Both of these species are plankton eaters and may exceed 50 pounds in size. Their impact on native species is not presently known, but they represent
a competitive threat to other plankton eating fish such as our native pearly life stages. Very young Asian carp in these river systems can be easily mistaken as shad or skipjack herring. All bait collectors using cast or dip nets should never dispose of any live bait into other water bodies due to the potential threat of spreading these aquatic
nuisance species.
Zebra mussels—A tiny D-shaped mollusk well established in some lakes. It can clog water intake pipes, damage vessel engines, obscure historic shipwrecks, and alter native species populations. Adult zebra mussels can attach to be moved on vessel hulls, engines, and other equipment. Microscopic larvae can get trapped and moved in water of vessel engines. Bilges, bait buckets, and live wells. Kentucky has zebra mussels present in our waters and are at nuisance levels in the Ohio River. They attach themselves to any solid submerged surface in a cluster, reproduce rapidly, and pose a serious threat to native freshwater mussel populations. These mussels have elongated pointed shells less than two inches long with a zebra like pattern of stripes. Zebra mussels can live 8 to 10 days out of water and can be transported to another water body while attached to a boat.
Hydrilla is an exotic plant invading Kentucky through transfer of plant fragments by boats and personal watercraft. All it takes is a small fragment of the plant to start a new colony. This plant forms extremely dense mats that grow to the surface of the waterbody making boating and swimming difficult. It literally fills shallow areas from top to bottom with vegetation. Hydrilla also chokes out native plants and displaces fish. It is extremely difficult to eradicate once it becomes established.

## Slide 17: Boating Accident Reporting
Stop, render aid and provide contact information.
Report is required when –
1. Death or personal injury requiring medical treatment beyond first aid
2. Damage to property in excess of $500.
Loss of life or missing person – must report within 48 hours, otherwise within 5 days.
Notes: KY Accident Reports.
The operator of any vessel involved in a collision, accident, or other casualty has a duty to render aid to others that were involved or affected by the collision or accident if they can do so without serious damage to his or her own vessel, crew or passengers. The aid rendered should be that which may be practicable and necessary in order to save them from or minimize any danger caused by the incident.
The operator of any vessel involved must provide his or her name, address, and vessel registration to any person who was injured during the incident and to the owner of any property damaged by the incident.
The operator of any vessel involved in a collision, accident, or other casualty which results in death or personal injury that requires medical treatment beyond first aid, or damage to property in excess of five hundred dollars ($500) must file a full description of the incident with the Kentucky Dept. of Fish & Wildlife Resources Law Enforcement Division on Kentucky Boating Accident Report Form.
An accident report in a case involving a loss of life must be submitted to the Department within forty-eight (48) hours of the incident.
An accident report in a case involving a reportable injury or property damage as described above must be submitted to the Department within five (5) days of the incident.
An accident report must be submitted in person or by mail to the Kentucky Department of Motor Vehicles, 120 State Street, Montpelier, KY 05063-0001.

## Slide 18: Boating Accident Reporting
REPORT TO:
Kentucky Dept. of Fish & Wildlife Resources
Law Enforcement Division
#1 Sportsman’s Lane
Frankfort, KY 40601
1-800-858-1549
Notes: Accident Reports.
File a full description of the incident with the Kentucky Dept. of Fish & Wildlife Resources Law Enforcement Division on a Kentucky Boating Accident Report Form.

## Slide 19: DFWR Contact
You may contact the DFWR by writing to the following address. KY Dept of Fish & Wildlife Resources Division of Law Enforcement #1 Sportsman’s Lane Frankfort, KY 40601
1-800-858-1549
Notes: Contact the Kentucky Dept. of Fish & Wildlife Resources Law Enforcement Division

## Slide 20: Thank you!
Any questions?
Find other Auxiliary boating courses at http://www.cgaux.org/boatinged
Request a vessel safety check at http://www.safetyseal.net
Learn more about joining the Auxiliary at: http://join.cgaux.org