## Slide 1: Maine Supplement
For use with Boat America and Boating Skills & Seamanship

## Slide 2: Boating References
Notes: The final examination includes a ten-question Maine supplemental assessment of learning regulations discussed in this section.
Some definitions:
No Wake Speed - a vessel may not operate in excess of the idling speed or the slowest possible speed necessary to maintain steerage under prevailing wind and water conditions.
No Wake Speed Zone - an area restricting motorboats from attaining a speed which would produce a wake that would noticeably disturb other motorboats or vessels, docks, piers, or any other shoreline facility within the designated area. This area should be marked by REGULATORY BOUYS or signs bearing the words ‘No Wake’.
Personal Watercraft or PWC - means a small Class A vessel which uses an outboard motor or an inboard motor powering a water jet pump as its primary source of motive power and which is designed to be operated by a person sitting, standing, or kneeling on, or being towed behind the vessel rather than the conventional manner of sitting or standing inside the vessel designed area.
Motorboats Which Carry Passengers for Hire Requirements
Motorboats which carry passengers for hire must be provisioned with a Type I personal floatation device for each person carried. They must also be provisioned with an additional number of Type I personal floatation devices suitable for children equal to at least ten percent (10%) of the maximum number of persons carried, unless the service is such that children are never carried. All personal floatation devices must be Coast Guard approved (see Personal Flotation Devices), must be maintained in a good and serviceable condition, and must be readily available for use at all times.
Motorboats carrying passengers for hire must be operated and navigated by a person duly licensed by the United States Coast Guard. This provision does not apply to whitewater outfitters and guides licensed under Maine Code, chapter twenty, article two [§20-2-23(a)] nor boating and canoeing outfitters and guides licensed under Maine Code, chapter twenty, article two [§20-2-26].
Motorboats carrying more than six (6) passengers must be inspected and certified by the United States Coast Guard.

## Slide 3: Boater Education
Beginning 1/1/2024, persons born on or after 1/1/1999 and operating a vessel capable of producing more than 25 HP power must:
  Be at least 12 years of age, and
  Complete a boater safety class, and
  Possess the boater safety card while boating
Notes: Who may operate a vessel in ME
Beginning January 1, 2024, the specifics regarding age of operation have changed. The next slide with present the specific break down regarding horsepower and age limits between a power boat and a PWC.

## Slide 4: Boater Education
Beginning 1/1/2024:
  Under 12 can operate up to 10 hp without supervision or boating safety course.
  Under 12 can operate over 10 hp with supervision.
  12 years and over can operate up to 25 hp without supervision or safety course.
  12 year and over can operate over 25 hp with a boating safety course.
  16 years and over must have a boating safety course to operate a PWC
  To supervise, if born after 1/1/1999, must be at least 16 years and over and have passed a boating safety course
Notes: Who may operate a vessel in ME
Operating a motorboat other than a PWC:
A person under 12 years of age may not operate a motorboat propelled by machinery of more then 10 horsepower unless under the immediate supervision of a person located in the motorboat who is at east 16 years of age. This does not apply to operating a PWC.
A person born on or after January 1, 1999, may not operate on inland water or territorial waters any motorboat for recreational boating purposes propelled by machinery capable of producing more than 25 horsepower unless that person is 12 years of age, and has completed a boating safety class, and possess and presets for inspection upon request to a law enforcement officer a boating safety education course certificate.
Operating a PWC:
Beginning January 1, 2024, a person born on or after January 1, 1999, may not operate a personal watercraft (PWC) on inland waters or territorial waters unless that person is16 years of age or older and has completed a boating safety education class.

## Slide 5: PWC Education
Persons under 16 years of age may not operate a PWC on Maine waters.
Persons aged 16 years of age and older may operate a PWC only if they:
  Have successfully completed an approved safety education course

## Slide 6: Boat Registration
Mechanically propelled boats must be registered with the Fish and Wildlife Office in Augusta.
Registration is valid for one year and expires on December 31 of the year when issued.
8 letters and numbers with validation decal
ME 2345 AB (decal)
Notes: Registration Requirements.
Motorboats (10hp or less) - $25.00
Motorboats (greater than 10hp, less than or equal to 50hp) - $30.00
Motorboats (greater than 50hp, less than or equal to 115hp) - $36.00
Motorboats (greater than 115hp) - $44.00
Personal Watercraft- $44.00
SECTION VIII. VESSEL REGISTRATION NUMBER
A. The number issued pursuant to these regulations shall be in accordance with the pattern described in this subsection.
1. The vessel registration number shall be divided into three parts, for the purpose of providing a combination of numerals and letters which furnish individual vessel registration numbers.
2. The first part of the number shall be an abbreviation in capital letters of the State of Maine – ME –and shall be followed by an equivalent space.
3. The second part of the number shall be a group of digits consisting of four Arabic numerals appearing after the letters ME, and shall be followed by an equivalent space.
4. The remainder of the number shall consist of no more than two capital letters, in sequence, in accordance with the serials numerically and alphabetically. As example:
5. Since the letters “I”, “O”, and “Q” may be mistaken for Arabic Numerals, all letters sequences using “I”, “O”, and “Q” shall be omitted. Objectionable words formed by the use of letters will not be used.

## Slide 7
Correct Display of Letters and Numbers
3’’ High
Contrasting colors
Sticker within 6 inches of ME Letters and Numbers
ME 2345 AB
ME 2345 AB
Port Side
Starboard Side
Notes: Display of numerals and decals on vessel.
1. The number awarded, exactly as shown on the certificate of numerals shall be painted on, or attached to, each side of the bow of the vessel for which it was issued.
2. The numerals shall be placed on each side of the forward half of the vessel in such position as to provide clear legibility for identification. The numerals shall read from left to right and shall be in block characters of good proportion not less than three inches in height. The numerals shall be of a color which will contrast with the background, and so maintained as to be clearly visible and legible; i.e., dark numerals on a light background or light numerals on a dark
background.
3. The commissioner will furnish to all applicants two (2) decals bearing the numbers of the year of expiration, which will establish valid registration. The decals are to be displayed on each side of the boat (within 6 inches) immediately following the assigned Maine number.
ME 0234 AB (decal) or ME-0234-AB (decal)

## Slide 8: Maximum Capacities
8
Capacity label by Manufacturer
Number of persons
Weight for persons, motor and gear
Maximum engine horsepower
Notes: Overloading and Overpowering.
No vessel may be loaded with passengers or cargo beyond its safe cargo carrying capacity.
The maximum persons capacity marked on a vessel's maximum capacities plate must not be exceeded.
The maximum weight capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe loading requirements.
Overpowering
No vessel may be operated beyond its safe powering capacity.
The maximum horsepower capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe powering requirements.

## Slide 9: Life Jackets
A USCG approved wearable personal flotation device (PFD) correctly sized and in serviceable condition is required to be on board for every person
Boats 16 feet and longer must additionally carry a USCG approved throwable device (not canoe or kayak)
Persons being towed, those 10 years and younger, and those aboard a PWC MUST wear a PFD
PFDs with water impact ratings are suggested for high-speed watersports such as operating PWC and being towed
Notes: ME Personal Flotation Devices (PFD)
All vessels, except sailboards, must carry one wearable U.S. Coast Guard-approved Type I, II, III, or V PFD for each person on board.
Ion addition, vessels 16 feet in length or longer must have one U.S. Coast Guard-approved Type IV PF on board and readily accessible.
Children 10 years of age and younger must wear a U.S. Coast Guard-approved.Type I, II, III, PFD at all times while underway on the open deck of any vessel.
Everyone on board a PWC must wear a U.S. Coast Guard-approved.Type I, II, III, PFD.
Anyone being towed behind a vessel must wear a U.S. Coast Guard-approved.Type I, II, III, PFD.

## Slide 10: Intoxication
A person is considered to be intoxicated if he or she:
• Has a blood concentration of 0.08% if age 21 years or older; or
Has any amount alcohol in their blood concentration if age under 21.

## Slide 11: Water Skis & Surfboards
All being towed must wear PFD
Allowed only between one-half hour before sunrise to one-half hour after sunset
The towing boat must have 12 year or older observer
Notes: ME Water Skis and Surfboards
No person May operate or manipulate any vessel, tow rope, or other device by which the direction or location of water skis, surfboards, or similar devices may be affected or controlled in such a way as to cause other water skis, surfboards, or similar devices, or any person thereon, to collide with or strike against any object or person.
No person may manipulate any water skis, surfboard, or similar device in a reckless or negligent manner so as to endanger the life, limb, or property of another person.
No person shall manipulate any water skis, surfboard or similar device while under the influence of alcohol or a controlled substance or drug, under the combined influence of alcohol and any controlled substance or any other drug, or while having an alcohol concentration in his or her blood .08 percent or more, by weight.
No person may operate a vessel towing a person on water skis, surfboard, or similar device, nor may any person engage in water skiing, surfboarding, or similar activity at any time between the hours from one-half hour after sunset to one-half hour before sunrise.
No person may operate a vessel towing a person on water skis, surfboard, or similar device unless:
A person at least twelve (12) years of age or older other than the operator is on board the vessel in a position to observe the progress of the person being towed;
No person may operate a personal watercraft (PWC) towing another person on water skis or other towables unless the personal watercraft has, on board, in addition to the operator, a rear-facing observer, who monitors the progress of the person or persons being towed. This rear-facing observer must be at least twelve years of age.

## Slide 12: Water Skis & Surfboards
Illegal to tow while intoxicated
Illegal to tow from a PWC.
Stay clear of no ski zones –
  No towing within 200 feet of commercial boat dock, moorage harbor, swim area
Notes: ME Water Skis and Surfboards
No person May operate or manipulate any vessel, tow rope, or other device by which the direction or location of water skis, surfboards, or similar devices may be affected or controlled in such a way as to cause other water skis, surfboards, or similar devices, or any person thereon, to collide with or strike against any object or person.
No person may manipulate any water skis, surfboard, or similar device in a reckless or negligent manner so as to endanger the life, limb, or property of another person.
No person shall manipulate any water skis, surfboard or similar device while under the influence of alcohol or a controlled substance or drug, under the combined influence of alcohol and any controlled substance or any other drug, or while having an alcohol concentration in his or her blood .08 percent or more, by weight.
No person may operate a vessel towing a person on water skis, surfboard, or similar device, nor may any person engage in water skiing, surfboarding, or similar activity at any time between the hours from one (1) hour after sunset to one (1) hour before sunrise.
No person may operate a vessel towing a person on water skis, surfboard, or similar device unless:
A person at least twelve (12) years of age or older other than the operator is on board the vessel in a position to observe the progress of the person being towed;
No person may operate a personal watercraft (PWC) towing another person on water skis or other towables unless the personal watercraft has, on board, in addition to the operator, a rear-facing observer, who monitors the progress of the person or persons being towed. This rear-facing observer must be at least twelve years of age.

## Slide 13: Signaling Devices
Mouth whistle or powered horn or whistle audible for one-half mile required for
boats less than 40 feet, including PWCs.
On state waters, boats greater than 40ft but less than 65 feet require a whistle or powered horn audible for 1/2mile.
On Federal waters, boats greater than 65.5 feet require a whistle and bell audible for 1 mile.
Notes: Signaling Devices
According to the NAVRULES, International rule states that if you have a vessel 100 meters or more, in addition it also must be provided with a gong, the tone and sound of which cannot be confused with that of a bell.
Gongs are for anchoring vessels greater than 100 meters.

## Slide 14: Safety Zones
On state waters, when traveling within 200 feet of the shoreline or an island, boaters must travel at headway speed.
Exception to headway speed limit includes fishing and waterskiing.

## Slide 15
MSD holds sewage
Some MSDs can treat sewage
Use pump out stations
ALL Maine waters are no discharge zones.
Type I and II Marine Heads must be sealed to prevent discharge
>>
15
Marine Sanitation
Devices (MSD)
Notes: MARINE SANITATION DEVICES
Motorboats with marine toilets are not allowed on public waters unless the toilet is equipped with a Type I, II or III marine sanitation device (MSD.) Type I and II MSDs chemically treat sewage. Type III MSDs are holding tanks for raw sewage.
Raw sewage shall not be discharged in any public waters. Type I and II MSDs must be sealed or locked while the vessel is on “no discharge” waters.

## Slide 16
International marine Pollution Law
Notes: No trash, garbage or waste overboard in waters of USA. This or similarly worded decal is to be applied to boats 26 feet and longer as reminder to not pollute. Applies to all boaters.

## Slide 17: Diving/Snorkeling Flags
The U.S. Coast Guard requires recreational vessels engaged in diving, scuba diving or snorkeling on federally controlled waters to display the alpha diver-down flag

## Slide 18: Oil / Fuel Spills
Spills reported immediately to;
US Coast Guard at 1-800-424-8802
Placard displayed for vessels 26 feet and longer’
Notes: Waste and Trash, continued
The discharge of oil and hazardous substances is strictly prohibited by the regulations issued under the Federal Water Pollution Control Act. This act requires all boats with propulsion machinery to have a capacity to retain oil mixtures onboard.
You are not allowed to discharge oil or hazardous substances.
You are not allowed to sump oil into the bilge of the boat without means for proper disposal.
You must discharge oil wastes to a reception facility.
On recreational boats a bailer or bucket is adequate.
You must immediately notify the U.S. Coast Guard if your boat discharges oil or hazardous substances in the water. Call toll free 1-800-424-8802. Report the discharge’s location, color, source, substances, size and time observed.
If your boat is 26’ or longer you must display a 5” x 8” placard made of durable material fixed in a conspicuous place in the machinery spaces, or at the bilge pump control station stating the following:

## Slide 19: Aquatic Invasive Species
Trailer boaters should remove visible mud, plants, fish or animals from boats and trailers prior to transport to another body of water.
Scrape any mussels from boat or outdrive, and flush hull, bilges & water holding compartments with hot water (use 1 quart / gal of vinegar).
Do not release plants or fish, including bait, into a body of water unless it came from same body of water.
To prevent the spread of non-native fish and mollusks in our waterways, boaters should follow these simple rules:
Notes: ME Aquatic Nuisances
Introducing non-native species into Maine waters can upset the balance of the ecosystem., harming the environment. Some common nuisance species found in Maine include Eurasian Watermilfoil, hydrilla, and zebra mussels:
Eurasian Watermilfoil—A prolific aquatic plant found in many inland lakes in Maine. It interferes with boating and displaces native plants. It is spread easily when plant fragments are caught and moved via boat trailers, propellers, anchors, or wet wells. Plant fragments can initiate new plants and become well established.
Zebra mussels—A tiny D-shaped mollusk well established in some lakes. It can clog water intake pipes, damage vessel engines, obscure historic shipwrecks, and alter native species populations. Adult zebra mussels can attach to be moved on vessel hulls, engines, and other equipment. Microscopic larvae can get trapped and moved in water of vessel engines. Bilges, bait buckets, and live wells.

## Slide 20: Boating Accident Reporting
Stop, render aid and provide contact information
Report required when –
1. Death or personal injury requiring medical treatment beyond first aid
2. Damage to property in excess of $2,000.
Loss of life-report immediately followed by written report within 24 hours, otherwise within 72 hours
Notes: ME Accident Reports.
The operator of any vessel involved in a collision, accident, or other casualty has a duty to render aid to others that were involved or affected by the collision or accident if they can do so without serious damage to his or her own vessel, crew or passengers. The aid rendered should be that which may be practicable and necessary in order to save them from or minimize any danger caused by the incident.
The operator of any vessel involved must provide his or her name, address, and vessel registration to any person who was injured during the incident and to the owner of any property damaged by the incident.
The operator of any vessel involved in a collision, accident, or other casualty which results in death or personal injury that requires medical treatment beyond first aid, or damage to property in excess of two-thousand dollars ($2,000) must file a full description of the incident with the Maine Wildlife Resources Authority on the Maine Boating Accident Report Form.
An accident report in a case involving a loss of life must be reported immediately followed by a written report submitted to the ME DIFW within twenty-four (24) hours of the incident.
An accident report in a case involving a reportable injury or property damage as described above must be submitted to the Department within five (5) days of the incident.
An accident report must be submitted in person or by mail to the ME Environmental Police Box 1325 Augusta ME.

## Slide 21: Boating Accident Reporting
REPORT TO:
Maine Department of Inland Fisheries and Wildlife
Augusta, ME
form is at www.ME.gov/ifw
Notes: Accident Reports.
File a full description of the incident with the Maine Department of Inland Fisheries on a Maine Environmental Police Boating Accident Report Form.

## Slide 22: Maine Contact
You may contact the ME Department of Inland Fisheries by writing to the following address.
Main Office
284 State Street
41 Statehouse Station Augusta, ME 04333-0041
207-287-8000
Notes: Contact the Maine Department of Inland Fisheries Augusta, ME

## Slide 23: Thank you!
Any questions?
Find other Auxiliary boating courses at http://www.cgaux.org/boatinged
Request a vessel safety check at http://www.safetyseal.net
Learn more about joining the Auxiliary at: http://join.cgaux.org