## Slide 1: Montana Supplement
For use with Boat America and Boating Skills & Seamanship

## Slide 2: Boating References
Material for this supplement is contained in the publication:
Montana Boating Laws
The PDF can be downloaded at:
https://fwp.mt.gov/activities/boating/rules-regulations
Notes: Material for this power point program was sourced from the this reference. The final examination includes a ten-question Montana supplemental assessment of learning regulations discussed in this section.

## Slide 3: Mandatory Education
Persons 12 years of age and younger may not legally operate any motorized vessel over 10 horsepower, including PWC, unless accompanied on board by a person at least 18 years of age.
Persons 13 to 14 years of age may legally operate a motorized vessel over 10 horsepower, including PWC, only if they:
  Possess a Montana boating safety certificate or other NASBLA approved safe boating class, or
  Is accompanied on board by a person 18 years or older.

## Slide 4: Mandatory Education
A person must be at least 18 years of age to rent a motorized vessel over 10 horsepower, including PWCs.
Operators required to have a boater education certificate must carry it on board the vessel.

## Slide 5: Boating Accident Reporting
Operators involved in a collision must stop and offer assistance.
Provide, in writing to the owner of damaged property or anyone injured, his/her name, address, and vessel identification information.
Report accidents on report forms to a local Montana Fish, Wildlife, and Parks office.

## Slide 6: Boating Accident Reporting
Accidents must be report if:
  it caused the death or disappearance of any person;
  it caused an injury requiring medical treatment beyond first aid;
  it caused property damage in excess of $100.

## Slide 7: Boating Registration
A Montana Certificate of Number (registration) and validation decals are required to operate sailboats 12 feet or longer and all powered vessels on Montana public waters. Exceptions are:
  All manually-propelled vessels;
  Boats registered in other state operating on Montana waters for no more than 90
  consecutive days;
  Vessels documented with the US Coast Guard.
• The registration certificate must be on board and
available for inspection.

## Slide 8: Boating Registration
Registration number and decals must be displayed as follows:
  Number must be painted, applied as a decal, or otherwise affixed to the forward half of each side;
  No other numbers may be displayed on either side of the bow;
  Number is read from left to right on both sides;
  Number must be at least 3-inch-high BLOCK letters;
  Number’s color must contrast with the background.

## Slide 9: Boating Registration
Registration number and decals must be displayed as follows:
  Letters must be separated from the numbers by a space or hyphen, e.g., MT 234 ABC or MT-234-ABC;
  State decals include one permanent registration decal and two validation decals.
  The permanent registration decal is attached to the port side of the vessel, 3 inches aft and in line with vessel number.
  The two validation decals are attached on each side of the vessel aft of the vessel number.

## Slide 10
Correct Display of Numbers
3’’ High
Contrasting colors
Validation Decal AFT of MT Number
Permanent Decal port side of the number.
MT 2345 AB
MT 2345 AB
Port Side
Starboard Side

## Slide 11: Boating Registration
  All vessels that require registration must also be titled in Montana
  Vessels must apply for title within 40 days of purchase or transfer;
  Validation decals are good for 3 years;
  Permanent registration decals have no expiration;
  Larger vessels may be documented by the US Coast Guard.

## Slide 12: Maximum Capacities
12
Capacity label by manufacturer
Number of persons
Weight for persons, motor and gear
Maximum engine horsepower
Copyright 2018 Coast Guard Auxiliary Association

## Slide 13: Life Jackets
A USCG approved PFD is required to be on board for every person.
Boats 16 feet and longer must additionally carry a USCG approved throwable device, except canoes or kayaks.
Children under age 12 must wear an approved life jacket while on any vessel less than 26 feet long when in motion.
Each person on a PWC must wear a PDF.
Persons towed behind a vessel must wear a PFD.
A Type V PFD may be substituted for other PDFs if approved for the activity.

## Slide 14: Personal Watercraft
Must be at least 13 to operate.
If 13 or 14 years old, must have passed a boater safety class or be accompanied on board by a person 18 years or older.
Everyone on board PWC must wear USCG approved Type I, II, or III PDF.
PWC operator must attach the lanyard of the ignition safety switch to his/her wrist of PFD
Must maintain “no wake speed” within 200 feet of a dock, swimmer, swimming raft, non-motor vessel, or anchored vessel.

## Slide 15: Personal Watercraft
When towing a person on any device, a PWC must have an observer or spotter on board.
A PWC may not be rented to anyone under 18 years old.
One USCG approved Type B-1 fire extinguisher must be on board.
All rules regarding safe operation of a boat apply to PWC.

## Slide 16: Personal Watercraft
Stand-up PWC and PWC towing a water-skier must travel at the minimum speed necessary to operate when leaving from or returning to a dock or shore.

## Slide 17: Intoxication
Montana law prohibits anyone from boating while intoxicated. It is unlawful to operate or be in actual physical control of a motorboat, PWC, sailboat, water-skies, surfboard, or similar device while under the influence of alcohol or drugs

## Slide 18: Unlawful Operation
Reckless Operation is any failure to exercise the care necessary to prevent the endangerment of another person or property.
Weaving through congested traffic;
Passing unnecessarily close to another vessel;
Buzzing or wetting down others;
Operating or beaching within swimming areas;
Riding on the bow, gunwales, or transom;

## Slide 19: Unlawful Operation
Crossing or jumping the wake of another vessel within 100 yards of the vessel or within 100 yards of a water-skier or anything towed by the vessel, except when entering or leaving a marina or docking area.
Any reckless approach to or departure from, or passage by a dock, ramp, diving board, or float.
Pursue, flush or harass any wildlife or game animal.

## Slide 20: Unlawful Operation
Do not operate your watercraft
within 20 feet of exterior of a designated swimming area;
within 200 feet of a “diver-down” flag;
within 50 feet of a swimmer, expect boats towing water skiers, etc.
within 75 feet of person fishing or hunting waterfowl.
Failure or observe “no wake speed” areas. Operators are responsible for damage caused by their wake.

## Slide 21: Unlawful Operation
Lakes greater than 35 surface acres within the Western Fishing District:
Vessels limited to “no wake” speeds 200 feet from the shoreline;
PWCs maintain minimum operating speed through the “no wake” zone;
Motor vessels towing a skier must travel the most direct route through a “no wake” zone.

## Slide 22: Unlawful Operation
All vessels operating on public lakes and reservoirs in the Western Fishing District that 35 acre or less are limited to “no wake” speeds.

## Slide 23: Towed Persons
Persons being towed on water skis, or any other device must wear a US Coast Guard approved PFD.
In addition to the operator, a competent observer must be in the vessel (including PWC) to observe the progress of the person towed. If the vessel operator is 12 or younger, the observer must be at least 18.
Towing a person may only occur between sunrise and sunset.
Water skiers must not approach within 50 feet of swimmers or enter a designated swimming area..

## Slide 24: Diving/Snorkeling Flags
Boaters remain 200 feet away from a “diver” flag or vessels displaying the “alpha” flag.

## Slide 25
International Marine Pollution Law

## Slide 26: Oil/Fuel Spills
Spills reported immediately to;
US Coast Guard at 1-800-424-8802
Placard displayed for vessels 26 feet and longer’

## Slide 27: Aquatic Invasive Species
To prevent the spread of invasive species such as zebra mussels and Eurasian watermilfoil, operators should properly clean, drain and dry boats, trailers, and equipment after each use.
Boat operator must stop at all open watercraft inspection stations. Watercraft must be inspected before launching if:
Entering Montana from out of state.
Traveling west across the Continental Divide or into the Flathead Basin.

## Slide 28: Thank you!
Any questions?
Find other Auxiliary boating courses at: http://www.cgaux.org/boatinged
Request a vessel safety check at: http://www.safetyseal.net
Learn more about joining the Auxiliary at: http://join.cgaux.org