## Slide 1: For use with Boat America and Boating Skills & Seamanship
The Legal Requirements of Boating in Tennessee
Presentation Provided by the State of Tennessee

## Slide 2: Key Topics
Numbering and Documentation
Hull Identification Number
Age and Education Requirements
Unlawful Operation
Alcohol and Drugs
Obstructing Navigation

## Slide 3: Key Topics
Homeland Security
Personal Flotation Devices
Fire Extinguishers
Flame Arrestors, Ventilation, and Mufflers
Navigation Lights
Sound-Producing Devices
Visual Distress Signals

## Slide 4: Key Topics
Other Equipment and Regulations
PWC Laws
Laws Relating to Towing Persons
Waste, Oil, and Trash Disposal
Protecting the Environment
Reporting Accidents
Penalties and Enforcement

## Slide 5: Objectives
You should …
know which vessels need to be registered and how to do so.
be able to correctly place the Certificate of Number and validation decal on vessel.
know where to find the HIN number.
know the age and education restrictions for vessel operation.
Presentation Provided by the State of Tennessee

## Slide 6: Objectives
be able to list reckless and illegal behaviors that should be avoided when operating a vessel.
be able to explain dangers of consuming alcohol or drugs while boating, and penalties for doing so.
know the laws pertaining to obstructing navigation.
know you role in keeping waterways safe and secure.

## Slide 7: Objectives
be able to identify classifications and uses of personal flotation devices and state legal requirements.
know legal requirements for fire extinguishers, flame arrestors, ventilation systems, and mufflers.
know legal navigation light requirements.
know legal requirements for visual distress signals and sound producing devices.

## Slide 8: Objectives
know the requirements for other equipment, such as diver-down and skier-down flags.
understand the legal requirements specific to PWCs.
know the legal requirements for towing a skier with a vessel.
understand how to properly dispose of waste, oil, and trash and properly use MSDs.
know when and how to report a boating accident.

## Slide 9: Certificate of Number and Validation Decals
You must have a Tennessee Certificate of Number and validation decals to operate your vessel legally. Only exceptions are:
  vessels propelled only by paddles or oars.
  vessels registered in other states but using Tennessee waters for 60 days or less.

## Slide 10: Certificate of Number and Validation Decals
Certificate of Number and validation decals obtained by submitting proper application and fee
Certificate of Number must be on board and available for inspection by an enforcement officer whenever vessel is operated
Illegal to operate vessel or allow others to operate vessel unless it is registered and numbered

## Slide 11: Certificate of Number and Validation Decals
Display number and decal as follows: Number must be painted or applied as a decal to both sides of forward half of vessel where no other number may be displayed
  Number shall read from left to right
  Number must be at least 3"-high, plain vertical BLOCK letters

## Slide 12: Certificate of Number and Validation Decals
  Number’s color must contrast with background
  Letters must be separated from numbers by space or hyphen
  Decals must be placed to left or right of the registration number on both sides of bow

## Slide 13: Other Facts About Registration
Certificate of Number is valid for one, two, or three years, at option of owner
Owner of numbered vessel must notify TWRA within 15 days if:
  he or she changes address
  vessel is lost, stolen and/or recovered, destroyed, abandoned, or sold

## Slide 14: Other Facts About Registration
Vessels registered in another state may operate on Tennessee waters 60 consecutive days before Tennessee registration is required.
If Certificate of Number or decals is lost or destroyed, you must apply to TWRA for duplicate.
Larger recreational vessels owned by U.S. citizens may be documented by USCG. Documented vessels must also obtain Tennessee registration and carry Certificate of Number on board.

## Slide 15: Other Facts About Registration
Larger recreational vessels owned by U.S. citizens may be documented by USCG. Documented vessels must also obtain Tennessee registration and carry Certificate of Number on board.
Documented vessels must display the state decal on both sides of the vessel on the windows closest to the main operating station visible to enforcement officers.
Sailboats are to display the decals on both sides of the bottom f the main mast.

## Slide 16: Hull Identification Number
The Hull Identification Number (HIN) is a unique, 12-digit or 17-digit number assigned by the manufacturer to vessels built after 1972

## Slide 17: Hull Identification Number
Hull Identification Numbers:
  distinguish one vessel from another
  are engraved in the fiberglass or on a metal plate attached to the transom
  should be recorded and put in a safe place other than the vessel

## Slide 18: Who May Operate a Vessel
Those born after January 1, 1989
  Tennessee residents must successfully complete the TWRA Boating Safety Exam and carry on board the wallet Boating Safety Education Certificate issued by the TWRA while operating on Tennessee waters.

## Slide 19: Who May Operate a Vessel
  Non-residents within this age category must show proof of successful completion of any NASBLA–approved boating safety course
  Operators of vessels powered by engines of 8.5 hp or less and operators of sailboats under sail alone are not required to have certificate

## Slide 20: Who May Operate a Vessel
To operate a motorized vessel of more than 8.5 horsepower
  Those under 12 must have supervisor on board who is at least 18 and able to take immediate control of vessel. The supervisor, if born after January 1, 1989, also must have TWRA-issued Boating Safety Education Certificate.
  Those 12 or older operating alone must have TWRA-issued Boating Safety Education Certificate.
Those under 16 may not rent a PWC.

## Slide 21: Unlawful Operation
Reckless Operation of a vessel is any act which endangers life, limb, or property of another person. Examples are:
  Operating vessel in swimming area.
  Weaving vessel through congested waterway traffic.

## Slide 22: Unlawful Operation
  Steering toward another object or person in the water and swerving at last possible moment to avoid collision or spray others nearby
  Jumping wake of another vessel in a way that endangers another’s life, safety, or property
  Chasing, harassing, or disturbing wildlife with vessel

## Slide 23: Unlawful Operation
Improper Speed or Distance is not maintaining proper speed and distance while operating vessel. It is illegal to:
  operate at excessive rate of speed in crowded or dangerous areas or during periods of restricted visibility.
  operate at greater than “slow, no wake speed” in areas marked “No Wake.”
  operate within 300 feet of commercial vessel dock at greater than “idle speed.”
  jump wake of another vessel within 100 feet of that vessel.
  Vessels must be at no wake speed within 100 feet of any law enforcement vessel displaying blue flashing lights.

## Slide 24: Unlawful Operation
Riding on Bow, Gunwales, or Transom is allowing passengers to ride in places where there is a chance of falling overboard while underway at greater than idle speed

## Slide 25: Unlawful Operation
Unsafe Condition is operating vessel in condition that causes hazard to occupants or others on waterways. An enforcement officer may instruct operator to immediately take corrective action or return to nearest mooring if:
  there are insufficient PFDs, fire extinguishers, backfire arrestors, ventilation, or navigation lights.
  vessel is overloaded or overpowered.
  any other hazardous condition exists.

## Slide 26: Unlawful Operation
Boating Near Dams-Beware!
Take precautions when fishing below a dam by boat. Always wear a PFD and leave the motor running, even if drift fishing.
Never anchor boat in area below a dam and never anchor boat from the stern.
If a siren sounds or strobe lights flash, immediately move to safer area.
Presentation Provided by the State of Tennessee

## Slide 27: Alcohol and Drugs
Tennessee law prohibits anyone from boating under the influence (BUI)—that is, operating any motorized vessel while under the influence of alcohol or any combination of alcohol, controlled substances, or drugs
Alcohol and drugs cause impaired balance, blurred vision, poor coordination, impaired judgment, and slower reaction time
Alcohol is a major contributor to boating accidents and fatalities

## Slide 28: Alcohol and Drugs
By operating a vessel on Tennessee waters, you have consented to a sobriety test if requested by law enforcement officer.
Refusal to be tested is a separate offense and may result in loss of operating privileges for up to six months.

## Slide 29: Alcohol and Drugs
Tennessee law states that a person is presumed to be under the influence if concentration of alcohol in his or her blood is 0.08% or greater

## Slide 30: Alcohol and Drugs
Tennessee law establishes the following penalties
  Those convicted of boating under the influence are subject to a fine up to$2,500 for first or second offense and up to $5,000 for third offense
  In addition, those convicted of BUI may receive jail sentence up to one year (with mandatory probation) and lose operating privileges for one to ten years
  First conviction: sentenced to no less than 48 consecutive hours and no more than 11 month 29 days.
Notes: In addition to any fines, any person judged to be boating under the influence:
Commits a Class A misdemeanor.
Upon conviction of a first offense may be sentence to serve in the county jail or workhouse no less than 48 consecutive hours nor more than 11 months and 29 days.
Upon conviction of a first offense with a blood alcohol concentration of 0.20% or more, will serve a minimum of 7 consecutive days rather than 48 hours.
Upon conviction of a second offense, be sentenced to serve in the county jail or workhouse no less than 45 consecutive days nor more than 11 months and 29 days.
  In addition to the above, as a condition of probation the judge may also order participation in a substance abuse treatment program which includes any aftercare recommendation by the program, licensed or certified by the department of mental health and substance abuse services, including a certified drug court or DUI court, if the person first (a) completes a clinical substance abuse assessment and serves at least 25 days of the period of incarceration imposed by the county jail or workhouse.
Upon conviction of a third offense, be sentences to serve in the county jail or workhouse not less than 120 consecutive days nor more than 11 months and 29 days.
  In addition to the above, as a condition of probation the judge may also order participation in a substance abuse treatment program which includes any aftercare recommendation by the program, licensed or certified by the department of mental health and substance abuse services, including a certified drug court or DUI court, if the person first (a) completes a clinical substance abuse assessment and serves at least 65 days of the period of incarceration imposed by the county jail or workhouse.
Upon conviction of a fourth offense, shall be sentenced as a FELON and serve not less than 150 consecutive days nor more than the maximum punishment authorized for the appropriate range of a Class E felony.
Upon conviction of fifth offense for which prior convictions for vehicular assault, vehicular homicide, or aggravated vehicular homicide are to be included, shall be sentenced as a felon to serve not less than the minimum sentence of imprisonment established for a fourth offender, and not more than the maximum punishment authorized for the appropriate range of Class D felony.
Upon conviction of a sixth or subsequent offense, including any other applicable prior conviction described above, is a Class C felony and shall be sentenced to serve no less than the minimum sentence of imprisonment established for a fourth offender, and not more than the maximum punishment authorized for the range appropriate for a Class C felony.

## Slide 31: Alcohol and Drugs
Tennessee law establishes the following penalties
  First conviction if BAC is 0.20% or more sentenced to no less than 45 consecutive days and no more than 11 months and 29 days.
  Second conviction: sentenced to no less than 45 consecutive days and no more than 11 month 29 days. In addition a treatment program could be ordered.
  Third conviction: sentenced to no less than 120 consecutive days and no more than 11 month 29 days. In addition a treatment program could be ordered.
Notes: In addition to any fines, any person judged to be boating under the influence:
Commits a Class A misdemeanor.
Upon conviction of a first offense may be sentence to serve in the county jail or workhouse no less than 48 consecutive hours nor more than 11 months and 29 days.
Upon conviction of a first offense with a blood alcohol concentration of 0.20% or more, will serve a minimum of 7 consecutive days rather than 48 hours.
Upon conviction of a second offense, be sentenced to serve in the county jail or workhouse no less than 45 consecutive days nor more than 11 months and 29 days.
  In addition to the above, as a condition of probation the judge may also order participation in a substance abuse treatment program which includes any aftercare recommendation by the program, licensed or certified by the department of mental health and substance abuse services, including a certified drug court or DUI court, if the person first (a) completes a clinical substance abuse assessment and serves at least 25 days of the period of incarceration imposed by the county jail or workhouse.
Upon conviction of a third offense, be sentences to serve in the county jail or workhouse not less than 120 consecutive days nor more than 11 months and 29 days.
  In addition to the above, as a condition of probation the judge may also order participation in a substance abuse treatment program which includes any aftercare recommendation by the program, licensed or certified by the department of mental health and substance abuse services, including a certified drug court or DUI court, if the person first (a) completes a clinical substance abuse assessment and serves at least 65 days of the period of incarceration imposed by the county jail or workhouse.
Upon conviction of a fourth offense, shall be sentenced as a FELON and serve not less than 150 consecutive days nor more than the maximum punishment authorized for the appropriate range of a Class E felony.
Upon conviction of fifth offense for which prior convictions for vehicular assault, vehicular homicide, or aggravated vehicular homicide are to be included, shall be sentenced as a felon to serve not less than the minimum sentence of imprisonment established for a fourth offender, and not more than the maximum punishment authorized for the appropriate range of Class D felony.
Upon conviction of a sixth or subsequent offense, including any other applicable prior conviction described above, is a Class C felony and shall be sentenced to serve no less than the minimum sentence of imprisonment established for a fourth offender, and not more than the maximum punishment authorized for the range appropriate for a Class C felony.

## Slide 32: Alcohol and Drugs
Tennessee law establishes the following penalties
  Fourth conviction is sentenced as a FELON and will serve no less than 150 consecutive days and no more than maximum for a Class E felony.
  Fifth conviction with prior vehicular conviction added, results sentence no more than maximum authorized in range of Class D felony.
  Sixth or more convictions with prior vehicular conviction added, results sentence no more than maximum authorized in range of Class C felony.
Notes: In addition to any fines, any person judged to be boating under the influence:
Commits a Class A misdemeanor.
Upon conviction of a first offense may be sentence to serve in the county jail or workhouse no less than 48 consecutive hours nor more than 11 months and 29 days.
Upon conviction of a first offense with a blood alcohol concentration of 0.20% or more, will serve a minimum of 7 consecutive days rather than 48 hours.
Upon conviction of a second offense, be sentenced to serve in the county jail or workhouse no less than 45 consecutive days nor more than 11 months and 29 days.
  In addition to the above, as a condition of probation the judge may also order participation in a substance abuse treatment program which includes any aftercare recommendation by the program, licensed or certified by the department of mental health and substance abuse services, including a certified drug court or DUI court, if the person first (a) completes a clinical substance abuse assessment and serves at least 25 days of the period of incarceration imposed by the county jail or workhouse.
Upon conviction of a third offense, be sentences to serve in the county jail or workhouse not less than 120 consecutive days nor more than 11 months and 29 days.
  In addition to the above, as a condition of probation the judge may also order participation in a substance abuse treatment program which includes any aftercare recommendation by the program, licensed or certified by the department of mental health and substance abuse services, including a certified drug court or DUI court, if the person first (a) completes a clinical substance abuse assessment and serves at least 65 days of the period of incarceration imposed by the county jail or workhouse.
Upon conviction of a fourth offense, shall be sentenced as a FELON and serve not less than 150 consecutive days nor more than the maximum punishment authorized for the appropriate range of a Class E felony.
Upon conviction of fifth offense for which prior convictions for vehicular assault, vehicular homicide, or aggravated vehicular homicide are to be included, shall be sentenced as a felon to serve not less than the minimum sentence of imprisonment established for a fourth offender, and not more than the maximum punishment authorized for the appropriate range of Class D felony.
Upon conviction of a sixth or subsequent offense, including any other applicable prior conviction described above, is a Class C felony and shall be sentenced to serve no less than the minimum sentence of imprisonment established for a fourth offender, and not more than the maximum punishment authorized for the range appropriate for a Class C felony.

## Slide 33: Obstructing Navigation
It is illegal to:
operate in such a way that will interfere with safe navigation of other vessels
anchor in traveled portion of river or channel preventing or interfering with any vessel passing through area
moor or attach vessel to buoy, beacon, light, or any other navigational aid
move, displace, tamper with, damage, or destroy any navigational aid
obstruct a pier, wharf, boat ramp, or access to any facility
Presentation Provided by the State of Tennessee

## Slide 34: Homeland Security
Do not approach within 100 yards and slow to minimum speed within 500 yards of any U.S. Naval vessel. If you need to pass within 100 yards of a U.S. Naval vessel for safe passage, must contact the U.S. Naval vessel or USCG escort vessel on VHF-FM channel 16.

## Slide 35: Homeland Security
Observe and avoid all security zones. Avoid commercial port operation areas.
Observe and avoid other restricted areas near dams, power plants, etc.
Do not stop or anchor beneath bridges or in channels.
Watch for anything that looks peculiar or unusual.
Report suspicious activities.

## Slide 36: Personal Flotation Devices (PFDs)
All vessels must be equipped with USCG–approved life jackets called personal flotation devices or PFDs
Quantity and type depends on:
  length of vessel
  number of people on board and/or being towed
Each PFD must be:
  in good condition and readily accessible
  proper size for the intended wearer
Boat operators should ask everyone to wear a PFD
Presentation Provided by the State of Tennessee

## Slide 37: Personal Flotation Devices (PFDs)
Type I: Offshore Life Jackets (Wearable Life Jacket)
For rough or remote waters where rescue may take awhile
Excellent for flotation—will turn most unconscious persons face up in water

## Slide 38: Personal Flotation Devices (PFDs)
Type II: Near-Shore Vests (Wearable Life Jacket)
Good for calm waters and fast rescues
May lack capacity to turn unconscious wearers face up

## Slide 39: Personal Flotation Devices (PFDs)
Type III: Flotation Aids (Wearable Life Jackets)
Good for calm waters and fast rescues
Will not turn most unconscious persons face up
Some designed to inflate when you enter water

## Slide 40: Personal Flotation Devices (PFDs)
Type IV: Throwable Devices
Cushions or ring buoys designed to be thrown to someone in trouble
Not for long hours in rough waters, non-swimmers or the unconscious

## Slide 41: Personal Flotation Devices (PFDs)
Type V: Special-Use Devices (Wearable Life Jackets)
Designed for specific activities
Some designed to inflate when you enter water
To be acceptable, Type V PFDs must be used in accordance with their label

## Slide 42: PFD Requirements
All vessels must carry at least one wearable Type I, II, III, or V USCG–approved PFD for each person on board.
In addition, one Type IV (throwable) USCG–approved PFD must be on board and immediately available on vessels 16 feet or longer (except canoes and kayaks).
All PFDs must be in good and serviceable condition and must be readily accessible. PFDs must be of the proper size for the intended wearer. Sizing is based on body weight and chest size.

## Slide 43: PFD Requirements
Children 12 and younger must wear a USCG–approved life jacket at all times while on the open deck of a recreational vessel that is not anchored, moored, or aground
A USCG–approved life jacket must be worn by each person on board vessels being operated within specifically marked areas below dams

## Slide 44: PFD Requirements
Each person on board a PWC must wear a USCG–approved wearable Type I, II, or III PFD.
Inflatable PFDs are not approved for PWC use, whitewater activities, or persons younger than 16. Not recommended for non-swimmers.
A ski belt may not be counted as one of the required PFDs on board your vessel. A ski belt may be worn while skiing, but an approved PFD for the skier must be on board the vessel.

## Slide 45: PFD Requirements
An emergency situation (rough water, rapid onset of bad weather, or dangerous boating traffic) can occur suddenly—leaving little or no time to put on life jackets.
Life jackets are very difficult to put on once you are in the water. Be a smart boater, and have everyone on board your vessel wear their life jackets at all times.

## Slide 46: Fire Extinguishers
Extinguishers are classified by a letter and number symbol
Number indicates the relative size of the extinguisher
Letter indicates type of fire it will extinguish
  Type A: Fires of combustible solids like wood
  Type B: Fires of flammable liquids like gasoline or oil
  Type C: Electrical Fires

## Slide 47: Fire Extinguishers
All vessels required to have a Type B fire extinguisher(s) on board if any of the following conditions exist:
  Vessel is 26 feet or longer
  Vessel carries passengers for hire
  Vessel has closed compartments under thwarts or seats where portable fuel tanks may be stored

## Slide 48: Fire Extinguishers
  Vessel has double bottoms not sealed to the hull or which are not filled completely with flotation material
  Vessel has closed living spaces
  Vessel has closed storage compartments where combustible or flammable materials may be stored
  Vessel has permanently installed fuel tanks

## Slide 49: Fire Extinguishers
Fire Extinguisher Requirements
Vessels less than 26 feet:
  without fixed system: one B-I
  with fixed system: none
Vessels 26 feet to less than 40 feet:
  without fixed system: two B-I or one B-II
  with fixed system: one B-I
Vessels 40 feet to less than 65 feet:
  without fixed system: three B-I or one B-II & B-I
  with fixed system: two B-I or one B-II
Presentation Provided by the State of Tennessee

## Slide 50: Fire Extinguishers
Approved fire extinguishers identified by “Marine Type USCG Approved” on the label, followed by size and type symbols and approval number
Inspect extinguishers regularly
Extinguishers should be readily accessible
Know how to operate them
On a PWC, fire extinguisher may not be easily accessible—should swim away quickly and use another operator’s extinguisher

## Slide 51: Backfire Flame Arrestors
Backfire flame arrestors must be:
In good and serviceable condition
U.S. Coast Guard–approved (must comply with SAE J-1928 or UL 1111 standards)
Periodically clean and check for damage

## Slide 52: Ventilation Systems
The purpose of ventilation systems is to avoid explosions by removing flammable gases. Properly installed ventilation systems greatly reduce the chance of a life-threatening explosion.

## Slide 53: Ventilation Systems
All gas-powered vessels that would entrap fumes must have at least two ventilation ducts fitted with cowls to remove the fumes
If vessel is equipped with power ventilation system, turn on for at least 4 minutes:
  after fueling
  prior to starting engine
If vessel not equipped with power ventilation system, open engine compartment and sniff for gasoline fumes before starting engine

## Slide 54: Mufflers
All vessel engines must be equipped with an effective muffling device. Vessel operators may not hear sound signals or voices if the engine is not adequately muffled.
Noise level of any motorized vessel must not exceed 86 decibels at distance of 50 feet or more from the vessel.
Use of cut-outs is prohibited.
Illegal to modify muffling system if it results in noise level greater than legal limit.

## Slide 55: Navigation Lights
Vessel operators must make sure vessels are equipped with proper navigation lights and use them:
  when away from dock between sunset and sunrise
  during periods of restricted visibility
No other lights that may be mistaken for required navigation lights may be exhibited
Blue or red flashing lights are restricted to use by law enforcement vessels
The requirements for navigation lights differ depending on type and size of vessel

## Slide 56: Navigation Lights
Power-Driven Vessels (including sailboats operating under power) less than 65.6 feet long when underway must exhibit:
red and green sidelights visible from a distance of at least two miles away—or if less than 39.4 feet long, at least one mile away—on a dark, clear night
an all-round white light or both a masthead light and a sternlight visible from a distance of at least two miles away on a dark, clear night
the all-round white light (or masthead light) must be at least 3.3 feet higher than the sidelights
Presentation Provided by the State of Tennessee

## Slide 57: Navigation Lights

## Slide 58: Navigation Lights
When underway, unpowered Vessels less than 65.6 feet long must exhibit:
red and green sidelights visible from a distance of at least two miles away—or if less than 39.4 feet long, at least one mile away—on dark, clear night
stern light visible from at least two miles away
Presentation Provided by the State of Tennessee

## Slide 59: Navigation Lights
When underway, unpowered Vessels less than 23 feet long must exhibit:
if practical, same lights as required for unpowered vessels less than 65.6 feet in length
if not practical, at least one lantern or flashlight shining a white light
Presentation Provided by the State of Tennessee

## Slide 60: Navigation Lights
When not underway, all vessels are required to exhibit a white light visible from all directions whenever moored or anchored away from dock between sunset and sunrise

## Slide 61: Visual Distress Signals
Visual Distress Signals (VDSs) allow vessel operators to signal for help in the event of an emergency
VDSs are classified as:
  day signals (visible in bright sunlight)
  night signals (visible at night)
  both day and night signals
VDSs are either:
  pyrotechnic (smoke and flames)
  non-pyrotechnic (non-combustible)

## Slide 62: Visual Distress Signals
If on federally controlled waters, vessel must be equipped with USCG–approved VDSs.
All vessels required to carry night signals when operating between sunset and sunrise. Most vessels must carry day signals also. Exceptions are:
  recreational vessels less than 16 feet in length.
  non-motorized open sailboats less than 26 feet in length.
  manually propelled vessels.
VDSs must be USCG–approved, in serviceable condition, and readily accessible.

## Slide 63: Visual Distress Signals
Pyrotechnic Visual Distress Signals
Non-Pyrotechnic Visual Distress Signals
Orange Smoke
Day & Night Signal
Day & Night Signal
Day Signal
Night Signal
Day Signal
Red Meteor
Red Flare
Electric Light
Orange Flag
Arm Signal
Presentation Provided by the State of Tennessee

## Slide 64: Visual Distress Signals
If pyrotechnic VDSs are used, minimum of three must be on board—must be dated and not used past expiration date. Examples that satisfy USCG requirements are:
  three hand-held red flares
  one hand-held red flare and two red meteors
  one hand-held orange smoke signal, two floating orange smoke signals, and one electric light
Prohibited to display visual distress signals except when assistance is required to prevent immediate or potential danger to persons on board

## Slide 65: Sound-Producing Devices
Sound producing devices are essential in periods of reduced visibility or whenever operator needs to signal his or her intentions or position.
When operating on Tennessee waters:
  Vessels less than 39.4 feet in length, including PWCs, are not required to carry a whistle or bell but must have some means to make an efficient sound signal.
  Vessels that are 39.4 feet or more in length are required to carry on board a whistle and a bell.

## Slide 66: Sound-Producing Devices
When operating on federally controlled waters:
  Vessels less than 65.6 feet in length, including PWCs, required to carry on board a whistle or horn or some other means to make an efficient sound signal audible for at least one-half mile
  Vessels that are 65.6 feet or more in length required to carry on board a whistle or horn, and a bell that are audible for at least one mile

## Slide 67: Other Equipment and Regulations
Diver-Down Flag: State law requires that scuba divers and snorkelers display a diver-down flag to mark the diving area.
Vessel operators must not operate within 50 feet of a displayed diver-down flag and must reduce speed to idle speed within 200 feet of the flag.
Scuba divers or snorkelers should not place a flag where it will obstruct traffic or create a hazard to navigation.

## Slide 68: Other Equipment and Regulations
Two types of flags are used to indicate diving activity.
  A rectangular red flag, at least 10 inches on any side, with at least a 1½-inch, white diagonal stripe running from upper left to lower right is required on state waters.
  A blue and white International Code Flag A (or Alfa flag), at least 3.3 feet high and visible from all directions, must be displayed on vessels on federally controlled waters. This flag indicates that the vessel is involved in a diving activity.

## Slide 69: Other Equipment and Regulations
Marine Permits: Permits from the TWRA required for tournaments, regattas, races, parades, and exhibitions that may restrict waterway navigation or require additional patrol by wildlife officers.
The free permit may be requested by applying to TWRA at least 30 days prior to event.

## Slide 70: Other Equipment and Regulations
TWRA Access Areas: Additional restrictions apply in these areas.
  Disorderly conduct and use of intoxicants or other behavior-modifying substances prohibited.
  Use of firearms prohibited except during regular hunting season. Target shooting prohibited at all times.
  Swimming from or near boat ramps or in a way that interferes with launching or removal of vessels is prohibited.

## Slide 71: Requirements Specific to PWCs
PWC operators must obey these laws, in addition to all other boating laws:
Everyone on board a PWC must wear a USCG–approved wearable Type I, II or III life jacket at all times. Inflatable PFDs not approved for use on PWC
There are age and education requirements for operators of PWC
PWC must be equipped with ignition safety switch—operator must attach lanyard to his/her wrist or PFD
PWC may be operated only during daylight hours

## Slide 72: Requirements Specific to PWCs
PWC must operate in a safe and responsible manner. Illegal to:
    Jump the immediate wake (within 100 feet) of another vessel.
    Weave through congested waterway traffic.
    Steer toward another object or person in the water and swerve at last possible moment to avoid collision or spray others.
    Operate close to boat ramps, docks, or shoreline at more than idle speed.
    Chase, harass, or disturb wildlife with PWC.

## Slide 73: Towing a Person Legally
Vessel and PWC operators towing person(s) on water-skis, a surfboard, or any other device must obey these laws:
Illegal for vessels or PWC to tow persons on water skis, a surfboard, or any other device between sunset and sunrise or during inclement weather

## Slide 74: Towing a Person Legally
Towing vessel must be able to observe towed person(s). The towing vessel must have either:
  Person at least 12, in addition to operator, on board observing towed person or …
  The required number of rearview mirrors:
    If towing vessel is PWC, must be equipped with two wide-angle rearview mirrors
    If the towing vessel is a boat, must be equipped with at least one wide-angle rearview mirror

## Slide 75: Towing a Person Legally
All persons towed behind vessel or PWC on water skis or any other device must wear adequate and effective PFD, buoyant vest, or life belt. If device worn by skier is not USCG–approved, an approved PFD must be on board towing vessel.
Operator of towing vessel and skier must not operate in manner which endangers safety of persons or property. Maintain safe speed and distance from other vessels, persons in the water, docks, piers, and shorelines.

## Slide 76: Waste, Oil, and Trash Disposal
It is Illegal to discharge untreated waste, oil, or trash into any state or federally controlled waters
  Sewage carries disease and is harmful to people, aquatic plants, and animals
  Trash thrown into water can injure swimmers and wildlife and plug engine cooling water intakes
  Pollution is unsightly and takes away from enjoyment of the water
The Refuse Act prohibits throwing, discharging, or depositing any refuse matter of any kind into U.S. waters

## Slide 77: Waste, Oil, and Trash Disposal
Discharge of Sewage and Waste
If you have a recreational vessel with installed toilet facilities, it should have an operable marine sanitation device (MSD) on board
A MSD is a separate mechanism attached to the marine toilet
There are three types of MSDs
Presentation Provided by the State of Tennessee

## Slide 78: Waste, Oil, and Trash Disposal
Type I and II MSDs
Usually found on large vessels
Waste treated with special chemicals to kill bacteria before waste is discharged
Have “Y” valves that direct waste overboard which must be secured so valve cannot be opened
Presentation Provided by the State of Tennessee

## Slide 79: Waste, Oil, and Trash Disposal
Type III MSDs
Provide no treatment and are either holding tanks or portable toilets
Collected waste should be taken ashore and disposed of in a pump-out station or onshore toilet

## Slide 80: Waste, Oil, and Trash Disposal
It is illegal to discharge raw (untreated) sewage into any public waters.
Public waters are classified as either “discharge” or “no discharge.”
Vessels 65 feet or less in length may use Type I, II, or III MSD. Vessels more than 65 feet in length must install a Type II or III MSD.
All installed MSDs must be USCG–certified.
Marinas and docks operating on public water must provide sewage removal service.

## Slide 81: Waste, Oil, and Trash Disposal
Discharge of Trash
It is illegal to dump garbage and plastics into federally controlled or state waters—litter can kill birds, fish, and marine mammals
Store trash in a container on board, then place in a proper receptacle after returning to shore
On federal waters, display a 4"x 9" Garbage Disposal Placard on any vessel 26 feet or longer to notify passengers and crew about pollution restrictions
Presentation Provided by the State of Tennessee

## Slide 82: Waste, Oil, and Trash Disposal
Discharge of Oil and Other Hazardous Substances
Illegal to discharge oil or hazardous substances
Illegal to dump oil into bilge of vessel without means for proper disposal
On recreational vessels, bucket or bailer is adequate for temporary storage prior to disposing the oil waste at approved facility
Presentation Provided by the State of Tennessee

## Slide 83: Waste, Oil, and Trash Disposal
Must immediately notify the USCG if your vessel discharges oil or hazardous substances in water
Must also call the TWRA and report the discharge
On federal waters, vessels 26 feet or longer must display a 5"x 8" placard near the bilge pump control station stating Federal Water Pollution Control Act’s law

## Slide 84: Waste, Oil, and Trash Disposal
Waste Management Plan
Ocean-going vessels 40 feet or longer with cooking and sleeping facilities must have written Waste Management Plan
The captain of the vessel is responsible for implementing the plan
The plan should identify the vessel’s name and home port
Presentation Provided by the State of Tennessee

## Slide 85: Waste, Oil, and Trash Disposal
Captain of vessel should post plan and include directives to all passengers and/or crew about:
  discharge of sewage and hazardous substances
  discharge of garbage and other food waste
  disposal of plastics, bottles, and cans
  reading applicable placards for additional information
  advising captain of oily discharges/diesel spills

## Slide 86: Stop Spread of Nuisance Species
Introducing non-native species into state waters can upset the balance of the ecosystem, harming the environment
Aquatic nuisance species like zebra mussels, quagga mussels, milfoil, and hydrilla most often spread between waterways by hitching a ride on vessels and trailers
When transplanted into new waters, these organisms proliferate, displacing native species and damaging the water resource

## Slide 87: Stop Spread of Nuisance Species
To prevent spreading aquatic nuisance species:
inspect your vessel and trailer, and remove any plants and animals you see before leaving the area.
drain your motor, live well, and bilge on land before leaving the area.
dispose of unwanted bait and other animals or aquatic plants in the trash
To remove or kill species that were not visible when leaving the area, wash your boat and equipment with hot water or air dry them for at least five days
Presentation Provided by the State of Tennessee

## Slide 88: Accidents and Casualties
An operator involved in a boating accident must:
  stop his or her vessel immediately at the scene of the accident and …
  assist anyone injured or in danger from the accident, unless doing so would endanger his or her own vessel or passengers and …
  give in writing his or her name, address, and vessel identification to anyone injured and to the owner of any property damaged by the accident

## Slide 89: Accidents and Casualties
Vessel operators involved in a reportable accident must notify TWRA immediately.
  Operator must report accident to TWRA within 48 hours if person dies or disappears, or someone is injured and requires medical treatment beyond first aid.
  Operator must report accident in writing to TWRA within ten days if damage exceeds $2,000.
Failure to report boating accident is a criminal offense and may result in prosecution by TWRA.

## Slide 90: Enforcement
It is the responsibility of TWRA to enforce and administer provisions of the Tennessee Boating Safety Act.
Enforcement officers are on the water to assist boaters as well as to enforce laws and provide control when necessary.

## Slide 91: Enforcement
Every officer of the agency has authority to stop and board any vessel. They may issue citations or, when necessary, may arrest on sight and without warrant, any person violating the Safety Act.
Most TWRA vessels can be recognized by the orange and green stripes and the words “WILDLFE RESOURCES” on the sides.
USCG has enforcement authority on federally controlled waters.