## Slide 1: The Weekend Navigator
Session 3
Underway Navigation

## Slide 2: The Weekend Navigator
Cruise Problem #2 Review

## Slide 4
C 233 M
C 250 M
S 18.0
C 197 M
C 187 M
C 283 M
S 18.0
S 10.0
S 12.0
S 12.0
1044
1059
1105
WPT TURN
1120
1140
Notes: Review Cruise Exercise #2 results. DR position symbols left off to reduce clutter. Distance entries may be shown—navigator’s choice.

## Slide 5: The Weekend Navigator
Underway with Paper Charts
Fig 8-15
Notes: GPS is addresses first, then paper charts.

## Slide 6: Correcting for Variation & Deviation
Compass reads 018° but Range plots as 005° T
. . . What Gives?
Fig 2-12
Notes: This and the next slide Introduce TVMDC + W. While the text uses M for all measurements, some students will have seen this in traditional navigation lessons.
The text doesn't use the traditional term “uncorrecting,” but instead refers to all adjustments for variation and deviation, whether going from T to C or C to T as “correcting.”
Using the variation shown on Chart 1, rounded to 016° W.

## Slide 7: Correcting for Variation & Deviation
T
True Bearing 005°
V
Variation 016° W
M
Magnetic Bearing 021°
D
Deviation 003° E
C
Compass Bearing 018°
DOWN
ADD
WEST
Tele-
Vision
Makes
Dull
Children
Add Wonder (Add West)
START
Notes: Traditional navigation memory device, taken from the BS&S course, Chapter 9.
This applies to Bearings, Headings, or Courses.

## Slide 8: Class Exercise-Taking Bearings
260 M
1030
What is the M bearing (taken with a hand bearing compass) from the blue boat to the copula? Label it as an LOP
Notes: Use Chart 1

## Slide 9: Class Exercise-Taking Bearings
M
Magnetic Bearing 260°
D
Deviation 007° W
C
Ship’s Compass Bearing 267°
If the boat is pointed at the copula, what will the compass read? Compass deviation is 007° W on that heading.
Notes: Assume that the handheld compass was at a different location than the ships compass, so the handheld had no deviation

## Slide 10: Class Exercise-Fixs
Use Chart 2
Your GPS is on the fritz! At 1312, you take a ship’s compass bearing on the the Standpipe by pointing the boat at it. What is the M bearing? What is your Lat. / Long.?
The Standpipe at Nobska Pt bears 330° C. Your Deviation Table gives 004° W deviation on this heading.

## Slide 11: Class Exercise
M
326°
D
004° W
C
330°
Standpipe
Can’t determine position with only one LOP

## Slide 12
326 M
1312
Notes: Graphical solution to the exercise. We’ll use this fix during Session 4.

## Slide 13: Class Exercise-Fixs
Use Chart 2
At 1312, you also take a ship’s compass bearing on the Radio Tower by pointing the boat at it. What is the M bearing and what is your Lat. / Long.?
The Radio Tower at Falmouth Heights bears 022° C. The deviation on this heading is 003° E.

## Slide 14: Class Exercise
M
025°
D
003° E
C
022°
Radio Tower
41° 29.7’ N 070° 36.5’ W

## Slide 15
326 M
1312
025 M
1312
1312
Notes: Graphical solution to the exercise. We’ll use this fix during Session 4.

## Slide 16: The Weekend Navigator
Underway with GPS
Fig 8-15

## Slide 17: Steps in Waypoint Navigation
Select and activate the waypoint
Double check that you have a pre-qualified path
Steer to the direction
on the GPS
Fig 8-3
Notes: The Highway page shown is very useful for the helmsman.
Waypoint is selected from a listing or a map screen

## Slide 18: Steps in Waypoint Navigation
Monitor your progress
Be alert as you approach your destination
Select and activate the next waypoint
Be careful with your numbers!
Notes: Double check waypoint entries and keep situational awareness.

## Slide 19: Staying on Course
Reasons why you may wander off course
  Steering to avoid visible obstacles
  Your boat yawing in waves
  Inattention at the helm
  Crosswinds
  Crosscurrent
Fig 8-12

## Slide 20: Staying on Course
How can I use a non-mapping GPS to tell where I am?
  Plot the Lat./Long. coordinates
  Bearing and distance to a waypoint
Monitor GPS data. See page 101.
Use Map or Highway Screen
Keep a “proper look-out”
Notes: Page 101. Briefly discuss data that can be monitored underway.

## Slide 21: Staying on Course
Highway Screen may be easier to use
  Stay in the center of the highway and “oversteer” to return to the center line

## Slide 22: Staying on Course
GPS or Not: Effects of wind or current
  Pushes away from intended course
  Can be a curved path instead of the straight course to destination
  Check position before going directly for the destination
Fig 8-19
Sailing vessels- greater effect
Notes: Introduced the term Trackline

## Slide 23: Staying on Course
Actual track is at an angle downwind or “down current”
The solution is to head upwind or “up current” and “Crab” along your course line
Fig 8-22

## Slide 24: Staying on Course
Cross-track error (XTE, XTK, or “off course”): The distance that you are off course either to port (L) or starboard (R) in nm or ft.
Fig 8-26
Notes: “Off Course” reading in nm or ft depending on how far the vessel is from the intended course line.

## Slide 25: Sailors Tacking Decisions
Useful for tacking decisions
Set start and destination waypoints
Set limits on cross track error

## Slide 26: Navigating in a Region
Make use of the map screen when navigating casually (i.e., not on a route or going to a WPT)
Set your zoom level to correspond with your speed
Don’t “outrun” your GPS
Notes: The map screen can be used exclusively for an entire trip. It invited watching the GPS screen too much. Invites neglecting watching the helm.

## Slide 27: Marking Objects
Avoid dependence on Private ATONS
Set waypoints to avoid hazards
Set waypoints at landmarks and use for bearings
Notes: Danger bearings and circles are addressed in Session 4.
The next topic is using bearings for keeping track & double-checking

## Slide 28: Keeping Track & Double-Checking
Fig 10-3

## Slide 29
THE ROYAL MAJESTY, JUNE 9, 1995
Notes: The complete 75 page NTSB report is available on the internet. PB97-916401, NTSB/MAR-97/0l
The Royal Majesty departed Bermuda enroute to Boston on June 9, 1995, with 1509 persons on board. Just prior to departure, a repairman damaged the cable between the GPS antenna and the receiver, interrupting the signal. Nobody noticed that the GPS wasn’t working. The ship was continuously steered by the autopilot using DR data from the GPS, not waypoint data. The bridge crew completely relied on the GPS, without backing it up with traditional navigation techniques. She ran aground the next morning, about 17 miles off course. No injuries, but $7 million in damages and lost revenue.

## Slide 30
Notes: Planned course.

## Slide 31
Notes: Intended track vice actual track.

## Slide 32
Notes: No injuries. $7 million in damage to vessel and lost revenue.
GPS antenna disconnected. Backup systems were ignored

## Slide 33: Keeping Track & Double-Checking
What’s the use for Bearings?
Quick Observations
  Habitually identify ATONs and landmarks
  Take bearings using the ship’s compass
    Remember to apply deviation!
    Result is a magnetic bearing
    Easy to compare with GPS
Periodically plot your quick bearings on a chart
Notes: Keeping track and double checking isn’t a one time event, but is a process that’s fundamental to all navigation actions underway.
Information regarding the cruise ship Royal Majesty is presented in the “Additional Slides” following the end of the presentation.

## Slide 34: Keeping Track & Double-Checking
Compare visual bearings with GPS
Plot your GPS location on a chart from time to time
  In open waters, once an hour is adequate
  More frequently at high speed, dangerous water, or in bad weather

## Slide 35: Planning As You Go with GPS
Figure out where you are
  Location along an active leg
  Bearing to a landmark
  Using a grid line
  Using a waypoint
Plot a safe path to the new destination

## Slide 36: ESTIMATE DISTANCE
It’s all in the hands
  Helps provide a mean to approximate angular difference
Offset from direct heading
  Used when you can not find a suitable landmark that lines up with your heading

## Slide 37: Collision Bearings
Use relative bearings to anticipate a collision
Constant bearing, decreasing range – watch out!!
Know the rules of the road- take appropriate action

## Slide 38: Collision Bearings
Fig 11-10

## Slide 39: What To Do If the GPS Quits
Notes: May not realize the GPS has quit or is in error unless the navigator is Double Checking.

## Slide 40: Stop and Regroup
Find your location
  Use landmarks or ATONs
  Use LOPs to get a fix
  Use a backup GPS
Fig 12-1
Fig 12-2

## Slide 41: Stop and Regroup
Other alternatives to finding position
  Reconstruct DR plot
  Depth and depth profile
  Radar
Fig 12-3

## Slide 42: Plan Before Proceeding
Plot your best estimate on your chart
Examine your charted path for hazards
Be prepared to seek alternative routes
Be Careful with the numbers!
Notes: Nearly 100% of navigation errors underway are due to carelessness.

## Slide 43: Navigating without GPS
Work-up a quick DR plot
Update your position from time to time using DR, Landmarks, and fixes
Fig 12-6

## Slide 44: The Weekend Navigator
Homework for Session 4
Chapters 14-15

## Slide 45: The Weekend Navigator
Additional Slides

## Slide 46: The Weekend Navigator
End Additional Slides